The Electric Helicopter Beginner's Guide

by Toshiyasu Morita (TMorita on the Ezone and Ikarus BBS)

Many thanks to all the people on the Ezone forums and the Ikarus BBS who have posted many helpful messages - many of these tips were taken from these excellent discussion forums!

This was originally a "Heli FAQ" suggested by Fred Bronk, but it grew into much more than a FAQ - so now it's called the Electric Helicopter Beginner's Guide.

Use this information at your own risk! I make no guarantees as to the validity of any of this information! If in doubt, double-check!

Electric Helicopter Beginner's Guide Index

1. How helicopters work

2. Things you should know before entering the r/c helicopter hobby

3. First helicopter selection guide

4. Recommended beginner configurations

5. Brushless motor upgrade paths

6. Helicopter parts selection

7. Support equipment

8. Simulators

9. Transmitters

10. Helicopter construction

11. Soldering technique

12. Basic setup

13. R/C helicopter rules/tips

14. Learning to fly - the steps

15. Tail-in hovering

16. Side-in and nose-in hovering

17. Additional orientation exercises

18. Transmitter idle-up setup for fast forward flight

19. Entering and exiting fast forward flight

20. Banked forward turns

21. Figure eights

22. Backwards flight

23. Banked backwards turns

24. Backwards exercises

25. Maintenance and crash repair

26. Troubleshooting common problems

27. Useful equations

28. Electric helicopter & parts vendors

29. Terminology

1. How helicopters work

A helicopter is basically a rock with a propeller elice. The only lift it

generates is from the main rotor, and it uses a tail rotor to avoid

yawing from the torque generated by the main rotor.

Un helicopter este de fapt un bolovan cu elice. Singurul lucru care-l face să se ridice este rotorul principal, şi foloseşte rotorul anticuplu pentru a anula cuplul generat de rotorul principal.

The main rotor is composed of: the main blades, the smaller blades

are called the flybar paddles (or subrotor in some cases), and the hub

which holds the blades and paddles to the main shaft.

Rotorul principal este compus din: palele principale, palele mici care se numesc si “lopăţele zburătoare” sau subrotor în anumite contexte, şi butucul care fixează palele de axul principal.

Beneath the main rotor hub is a device called a swashplate which

is connected by linkages to the flybar and maybe the main blades.

The swashplate is a mechanical device that transmits the mechanical

position of the servos to the main rotor hub parts which are rotating.

It allows the cyclic servos which are on the helicopter body to change

the pitch of the flybar paddles and the main blades as the blades

rotate.

Sub butucul rotorului principal se află un mecanism numit platou ciclic care este conectat prin cu nişte tije de subrotor şi de palele principale. Platoul ciclic este un dispozitiv mecanic care transmite poziţia servomecanismelor către palele principale în timpul rotaţiei. El permite servomecanismelor aferente platoului ciclic care se află montate pe corpul helicopterului să schimbe unghiul de înclinare al subrotorului şi al palelor principale.

The antirotation pin and the antirotation arm keep the bottom part

of the swashplate from rotating while the top portion rotates along

with the main rotor.

Acul şi braţul de antirotaţie ţine partea din faţă a platoului ciclic nemişcată faţă de componenta sa  care se roteşte deodată cu axul principal.

The cyclic servos are controlled by the radio, and control the tilt

(and for CCPM also the position) of the swashplate. There are usually

either two or three cyclic servos.

Servomecanismele platoului ciclic sunt pilotate de catre radiocomandă şi controlează poziţia platoului ciclic. În mod obiţnuit sunt două sau trei servomecanisme pentru platoul ciclic.

In a CCPM (Cyclic/Collective Pitch Mixing) system, the swashplate is

connected via series of mechanical linkages to the flybar and the main

rotor blade grips. The tilt of the swashplate controls the flybar

paddle attack angle as it rotates, and the height of the swashplate

as it slides up and down the main rotor shaft controls the angle of

attack of the main blades.

În sistem CCPM (Cyclic/Collective Pitch Mixing) platoul ciclic este conectat printr-o serie de legături mecanice la subrotor şi la legăturile palelor principale.

In a non-CCPM system (like the Piccolo CP), the swashplate is connected

only to the flybar, and a seperate series of linkages controls the

pitch of the main rotor blades. The tilt of the swashplate controls the

flybar attack angle as it rotates, and the swashplate does not slide

up and down the main rotor shaft.

În sistem non CCPM (similar cu cel de la Piccolo CP), platoul ciclic este conectat doar la subrotor, şi o serie separată de legaturi controlează înclinaţia palelor rototului principal. Înclinaţia platoului ciclic controlează unghiul de atac al subrotorului în timpul rotaţiei  şi nu se ridică sau coboară pe axul rotorului principal

In a fixed pitch system, the pitch of the main rotor blades cannot be

changed, so there are no linkages which control the pitch of the

main rotor blades.

În sistem cu inclinaţie fixă, înclinaţia palelor principale nu poate fi modificată, deci nu există legaturi care să controleze înclinaţia palelor principale.

The tail rotor prevents the helicopter body from yawing when the

helicopter motor drives the main rotor blades. The yaw varies as

the speed and pitch of the main blades change, so the amount of

tail rotor thrust is variable to compensate for this.

Rotorul de coadă (anticuplu) împiedică rotitea corpului elicopterului atunci când motorul elicopterului antrenează axul principal. Tendinţa de rotire variază în funcţie de schimbarea turaţiei sau înclinaţiei palelor principale, deci turaţia  rotorului anticuplu este variabilă pentru a compensa acest lucru.

Some helicopters use a fixed rotation rate/variable pitch tail rotor

system where the tail is driven by the same motor as the main rotor

via a belt, wire or tube drive. A tail servo changes the pitch of the

tail rotor blades to increase or decrease the tail rotor thrust.

Unele elicoptere folosesc “turaţie fixă / înclinaţie variabilă a palelor rotorului anticuplu” unde rotorul anticuplu este condus de motorul rotorului principal prin curea sau ax de transmisie. Un servomecanism anticuplu controlează în acest caz înclinaţia palelor rotorului anticuplu pentru a mări sau micşora unghiul acestora.

On other helicopters, the pitch of the tail blades is fixed but the

tail rotor blades are driven by a variable-speed electric motor

to provide the variable tail rotor thrust.

La alte elicoptere, inclinaţia palelor anticuplu este fixă dar rotorul anticuplu este acţionat de un motor electric cu turaţie variabilă pentru a realiza atacul rotorului anticuplu.

2. Before you enter the model helicopter hobby - things you should know.

2. Înainte de a începe pasiunea pentru elicoptere- lucruri care trebuie să la ştiţi

a. Helicopters require a SIGNIFICANT TIME COMMITMENT to

learn to fly.

a. Elicopterele necesită  un timp considerabil pentru a invăţa zborul

A helicopter is basically a radio-controlled UNICYCLE. It takes

a lot of time to develop a good sense of balance and orientation.

You will learn much faster if you can dedicate at least a half-hour

a day to practicing on a flight simulator.

Un elicopter este este defapt tot unitar radio-comandat. Necesita mult timp pentru a găsi un sens pentru balans si orientare. Veţi învăţa mult mai repede daca dedicaţi măcar o jumătate de oră pe zi antrenamentului pe un simulator de zbor.

In addition, helicopters require significant amounts of time to

build and isolate/fix various problems like vibration, tail wag,

and other problems that will develop.

În plus elicopterele necesita o durată de timp importantă pentru construţie şi pentru a izola/înlătura diferitele probleme ce apar ca de ex. vibraţii, oscilaţii ale cozii, şi alte probleme apărute.

b. Helicopters crash, and they are somewhat expensive to fix.

b. Elicopterele se prăbuşesc, şi sunt întrucâtva costisitoare în reparaţii.

Some helicopters are more durable than others, and some are

much cheaper to fix - these are good trainers. But, you cannot

expect to learn to fly without spending some money for repairs.

Be sure to allocate some money for repairs.

Unele elicoptere sunt mai durabile, iar altele sunt mai ieftine în reparaţii. Dar nu vă aşteptaţi să învaţaţi să zburaţi fără să cheltuiţi ceva pentru reparaţii. Asiguraşivă să alocaţi o sumă de bani pentru reparaţii.

c. It is really frustrating to learn how to hover.

Este dea dreptul anevoios să înveţi să “pluteşti” un elicopter.

Eventually, something will "click" inside your head, and you will

"get it". For some people, this occurs all of a sudden and

everything makes sense. For other people it seems to be a more

gradual process.

Eventual, un beculeţ se aprinde in mintea dvs. Şi atunci veţi înţelege. Pentru unii, dintr-o dată totul are sens. Pentru alţii pare să fie un proces mult mai îndelungat.

Basically, helicopters suck horribly. Then you get your first hover,

and it's an incredible headrush, and you're psyched for a whole week,

and you're hooked. :)

De fapt elicopterele acaparează oribil. Apoi reuşiţi primul zbor, şi deveniţi agitat, pentru toată săptămâna, deveniţi coroiat.

3. First Helicopter Selection

3. Prima alegere a unui elicopter

a. The three things to consider when selecting your first helicopter

are:

- Trei lucruri trebuie să luaţi în consideraţie când alegeţi primul elicopter:

1. Durability

2. Price of replacement parts

3. Availability of replacement parts

4. Size

- Durabilitatea

- Preţul la piesele de schimb

- Disponibilitatea pieselor de schimb

- Mărimea

The reason for this is: when you are learning to hover, you will crash.

This is a given. Everyone crashes. When you crash, you do not want to

spend a fortune repairing the helicopter, because everyone has limited

funds. When you crash, you do not want to wait forever for replacement

parts, because every day you spend waiting for a part is a day you are

not flying the helicopter, and learning something.

Motivul la toate acestea este că atunci când veţi învăţa să zburaţi, veţi avea accidente.

Asta este scis. Toată lumea are accidente. Când aveţi un accident, nu doriţi să cheltuiţi o avere reparând elicopterul, pentru că fiecare are un buget limitat. Când aveţi un accident, nu doriţi să aşteptaţi o veşnicie pentru piesele de schimb, pentru că orice zi în aşteptarea pieselor este o zi lipsită de zbor cu elicopterul, o zi fără a învăţa nimic.

Size is very important, because larger helis are more stable and easier

to hover. They have more inertia, so they move slower and they give more

warning of their intent. Micro helis are more difficult to hover because

they are very "skittish" and wander off in a new direction with very

little warning of their intent. Larger helis are not any easier to fly,

though.

Mărimea este foarte importantă, pentru că elicopterele mari sunt mult mai stabile si mai uşor de pilotat. Au inerţie mai mare, deci se mişcă mai încet şi îşi manifestă intenţia mult mai bine. Micro-elicopterele sunt mai dificil de pilotat pentru că sunt mai vioaie şi mai puţin sugestive în intenţiile lor. Totuşi, asta nu inseamna că elicopterele mari sunt uşor de pilotat.

If you live in an area like Seattle where it rains almost continuously

for nine months of each year, I would recommend a fixed-pitch Piccolo.

Otherwise the Lite Machines Corona is the best electric trainer

available today. The Corona is very stable and acts like a much

larger helicopter, so it is nearly ideal for learning hovering.

Daca locuiţi într-o zonă ploioasă unde plouă aproape tot timpul, vă recomand un Piccolo cu pas fix. De altfel şi Corona este cel mai bun elicopter electric pentru antrenament disponibil astăzi. Corona este foarte stabil şi reacţionează ca multe din elicopterele mari, deci este ideal pentru a învăţa pilotajul.

Also, GET A SIMULATOR. Even a free simulator such as FMS will save you

at least 100 dollars or so in replacement parts when learning hovering.

Achiziţionaţi  de asemenea şi un simulator. Chiar şi un simulator gratuit ca FMS vă va scuti de mulţi bani în timpul “şcolii de pilotaj”.

Recommended first heli choices:

Recomandări pentru alegera primului elicopter:

a. Corona (very durable, easier to hover, inexpensive)

b. Logo 10 (durable, easier to hover, expensive)

c. ECO Piccolo / Piccolo Fun (very durable, hard to hover, inexpensive)

d. Skylark (also sold as Feda Dragonfly, Century Hummingbird,

GWS Dragonfly, etc) (durable, hard to hover, inexpensive)

d. Voyager E (durable, easier to hover, expensive)

- corona (foarte durabil, uşor de pilotat, necostisitor)

- Logo 10 (durabil, uşor de pilotat, costisitor)

- ECO Piccolo / Piccolo Fun (foarte durabil, greu de pilotat, necostisitor)

- Skylark (şi sub denumirea de Feda Dragonfly, Century

Hummingbird, GVS Dragonfly, etc)  )durabil, greu de pilotat, necostisitor)

- Voyager E (durabil, uşor de pilotat, costisitor)

Not recommended for the first heli, but good for 2nd heli:

Nerecomandabil pentru primul elicopter, dar bun pentru al doilea:

a. Hornet FP/CP (fragile)

b. ECO Lite/8/16 (somewhat fragile)

c. Logo 16/20 (expensive)

d. Joker / Joker CX (expensive)

f. etc

- Hornet FP / CP (fragil)

- ECO Lite / 8 / 16 ( întrucâtva fragil)

- Logo 16 / 20 (costisitor)

- Joker / Joker CX (costisitor)

- Etc.

Overview of selected machines:

Consideraţii despre elicopterul selectat:

a. Lite Machines Corona

a. Lite Machines Corona

1. A very good trainer

2. Moderately inexpensive (retail about $180-$199)

3. Very durable

4. Manufacturer is in the US. Parts availability is very good.

5. 1250-1500 grams AUW, 610mm rotor diameter, 6-8 cells

6. large, moderate headspeed,

easy to learn hovering - not indoors in small venues (gym ok)

- Un foarte bun aparat de antrenament

- necostisitor mediu (preţ între 180-190 dolari)

- Foarte durabil

- Made in USA. Piesele se găsesc uşor.

- 1250-1500 grame AUW, rotorul principal 610mm , 6-8 celule

- turaţie moderată spre mare, uşor de învăţat pilotajul, dar nu în încaperi mici (în sîli de sport este OK)

b. Ikarus Fixed Pitch Piccolos (Fun or ECO)

b. Ikarus Fixed Pitch Piccolos (Fun or ECO)

1. Trainer, but harder to learn

(probably 50% harder than Corona)

2. Inexpensive (Fun retail ~$90, ECO retail ~$140)

3. Fairly durable but landing gear is flimsy;

requires reinforcement for beginners.

4. Manufacturer in Germany. Parts availability is good.

5. 280 grams AUW, 500mm main rotor diameter, 6-8 cells

6. small, low headspeed, hard to learn hovering,

- but can be flown indoors

- De antrenamnt, dar greu de învăţat (probabil 50% mai greu decât Corona)

- Necostisitor (FUN 90 dolari, ECO 140 dolari)

- Absolut durabil, dar cu trenul de aterizare fragil

- Made in Germany. Uşor de procurat piese de schimb

- 280 grame AUW, diametru rotor principal 500mm, 6-8 celule

- turaţia rotorului principal medie către mică, greu de învăţat pilotarea dar poate fi zburat in interior

The main differences between an ECO Piccolo and a Fun Piccolo

are:

Deosebirile principale între ECO Piccolo şi FUN Piccolo sunt:

1. The ECO Piccolo includes six ball bearings for the rotor

head, the main shaft, and the tail shaft.

The Fun Piccolo includes bushings instead.

2. The ECO Piccolo has CF main and tail rotor shafts.

The Fun Piccolo has steel main and tail rotor shafts.

The steel shafts run smoother than the CF shafts but they

are somewhat heavier

3. The ECO Piccolo includes tail motor connectors.

The Fun Piccolo includes with no tail motor connectors, and

the tail motor wires must be soldered directly to the

Piccoboard or the ESC wires.

4. The ECO Piccolo has a very lightweight tail boom.

The Fun Piccolo has a slightly heavier tail boom.

- ECO Piccolo are 6 rulmenţi în ansamblul rotor principal, ax principal, ax anticuplu. FUN Piccolo include un inventar stufos

- ECO Piccolo are ax principal şi ax anticuplu CF. FUN Piccolo are axele din oţel. Axele de oţel sunt mai rigide dar sunt şi ceva mai grele.

- ECO Piccolo are conectori pentru motorul anticuplu. FUN Piccolo nu are conectori şi trebuie lipite cablurile direct pe ESC.

- ECO Piccolo are o coada foarte uşoara şi fragilş. FUN Piccolo are coada puţin mai grea.

c. Ikarus Collective Pitch Piccolos (CP upgrade/Pro)

c. Ikarus Collective Pitch Piccolos (CP upgrade/Pro)

1. Medium to advanced flyers

2. Inexpensive (CP upgrade ~$99, Pro retail ~$199)

3. Fairly durable except for balsa main rotor blades (68213)

pitch arm base (68211) and landing gear.

4. Manufacturer in Germany. Parts availability is good.

5. 330 grams AUW, 540mm rotor diameter, 8-9 cells

6. small, high headspeed.

Not recommended to fly in house - headspeed too dangerous.

- Elicopter mediu spre avansat

- Necostisitor (upgrade la CP aprox 99 dolari, preţ de vâmzare 199 dolari)

- Absolut durabil cu excepţia palelor din balsa reper 68213, braţele pentru pas reper 68211 şi a trenului de aterizare

- Made in Germany. Piesele de schimb se găsesc uşor

- 330 grame AUW, diametru rotor principal 540mm, 8-9 celule

- Turaţie medie catre mare

- Nerecomandabil de zburat în casă – turaţie prea mare pentru locuri înguste

d. Ikarus ECO Lite:

d. Ikarus ECO Lite:

1. Only for experienced pilots - only does forward flight

2. Inexpensive (retail about $140)

3. Somewhat fragile, same weakness as ECO 8

4. Manufacturer in Germany. Parts availability spotty,

5. 1150 grams AUW, 760mm rotor diameter, 6-8 cells

6. doesn't hover. Forward flight only.

Difficult to learn to fly, outdoors only.

- Doar pentru piloţii experimentaţi – zboară doar înainte

- Necostisitor (aprox. 140 dolari)

- Relativ fragil, aceleaşi probleme ca la ECO 8

- Made in Germany. Piesele nu au totdeanua aceiaşi calitate

- 1150 grame AUW, diametru rotorului 760mm, 6-8 celule

- Nu ‘pluteşte’ zboară numai înainte. Dificil de învăţat. Numai pentru exterior.

e. Ikarus ECO 8

e. Ikarus ECO 8

1. Duration flying/slope soaring/moderate aerobatics capable

2. Moderately inexpensive (retail about $180)

3. Somewhat fragile - stock (non-hardened) main rotor shaft,

feathering shaft and tail rotor shafts bend easily,

frame and landing gear not very strong

4. Manufacturer in Germany. Parts availability spotty,

up to 4 weeks wait time for some parts.

5. 1300-1500 grams AUW, 1060mm rotor diameter, 6-12 cells

6. Large, high headspeed, easy to learn hovering, outdoors only

- Durata de zbor, plutire , bun pentru crobaţii medii

- Aproape necostisitor (aprox 180 dolari)

- Semifragil – in varianta de serie fără upgrade, axele se îndoaie foarte uşor, rama şi trenul de aterizare nu rea rezistente

- Made in Germany. Piesele nu au aceiaşi calitate, se aşteapta mult pentru piese

- 1300-1500 grame AUW, diametru rotor 1060mm, 6-12 celule

- Turaţie ridicată, uşor de pilotat, numai pentru exterior

f. Ikarus ECO 16

f. Ikarus ECO 16

1. Moderate to serious aerobatics capable

2. Moderately inexpensive (retail about $250)

3. Somewhat fragile - a little more than ECO 8 because

using the same parts for heavier helicopter

4. Manufacturer in Germany. Parts availability spotty,

up to 4 weeks wait time for some parts.

5. 2000 grams AUW, 1200mm rotor diameter, 12-20 cells

6. Large, high headspeed, easy to learn hovering, outdoors only

- Mediu către ridicat nivel de acrobaţie

- Mediu ca şi costuri ( aprox 250dolari)

- Semifragil -  ceva mai fragil ca ECO 8 pentru că foloseşte aceleaşi componente ca ECO 8 dar pentru un elicopter mai mare şi mai greu.

- Made in Germany. Piesele nu sunt de aceiaşi calitate. Se aşteaptă destul de mult la achiziţionarea lor

- 2000 grame AUW, diametru rotor 1200mm, 12-20 celule

- Turaţie ridicată, uşor de pilotat, numai pentru exterior.

g. Feda Skylark/Century Hummingbird/GWS Dragonfly

g. Feda Skylark/Century Hummingbird/GWS Dragonfly

1. Trainer, but harder to learn

(probably 50% harder than Corona)

2. Inexpensive - $80 for bare heli kit

3. Fairly durable, but rotor blades are stiffer?

than Piccolo and are more easily destroyed.

4. Manufacturer in Taiwan?. Parts availability is good.

5. 280 grams AUW

6. small, low headspeed, hard to learn hovering,

- but can be flown indoors

- Greu de învăţat. Probabil cu 50% mai greu decât Corona

- Necostisitor (80 dolari / kit)

- Foarte durabil, dar palele sunt mai rigide ca cele de Piccolo şi se distrug mai repede

- Made in Taiwan. Piesele se gasesc uşor.

- 280 grame AUW

- Turaţie mica, greu de invăţat pilotajul, dar poate zbura în interior.

h. JR Voyager E

h. JR Voyager E

1. Trainer/light aerobatics capable

2. Expensive (retail about $400 incl. motor,

cannot buy without motor)

3. About average durability

4. Manufacturer in Japan. Parts availability very good.

5. 1500 grams AUW, 965mm rotor diameter, 7 cells

6. large, high headspeed, easy to learn hovering, outdoors only

- De antrenament, capabil de acrobaţii moderate.

- Costisitor (aprox 400 dolari cu motor inclus, nu se poate cumpăra fără motor)

- Durabilitate medie.

- Made in Japan. Piesele se găsesc foarte uşor.

- 1500 grame AUW, diametru rotor 965mm, uşor de pilotat, doar pentru exterior.

i. Kyosho Concept EP - discontinued?

i. Kyosho Concept EP – nu se mai fabrică?

1. Trainer/light aerobatics

2. Expensive (retail about $380 incl motor,

cannot buy without motor)

3. About average durability

4. Manufacturer in Japan. Parts availability ?

5. 1500 grams AUW , 912mm rotor diameter, 7 cells

6. large, high headspeed.

Has weak power due to high disc loading.

Flapping head version is very prone to boom strikes.

- Bunde antrenament, capabil de crobaţii moderate.

- Scump (aprox. 380 dolari cu motor inclus, nu poate fi cumpărat fără motor

- Durabilitate medie.

- Made in Japan. Piesele se găsesc uşor ?

- 1500 grame AUW, diametru rotor 912mm, 7 celule

- Turaţie ridicată, putere mică datorită incărcăturii discului.

i. Mikado Logo 10

i. Mikado Logo 10

1. Trainer/moderate aerobatics capable

2. Expensive (retail about $340)

3. About average durability

4. Manufacturer in Germany. Parts availability okay.

5. ~2500 grams AUW, 1150mm rotor diameter, 10-14 cells

6. large, high headspeed, easy to learn hovering, outdoors only

- Antrenament şi capabil de acrobaţii  moderate

- Costisitor (aprox 340 dolari)

- Durabilitate medie

- Made in Germany. Piese se găsesc uşor

- aprox 2500 grame AUW, diametru rotor 1150mm, 10+14 celule

- turaţie ridicată, uşor de invăţat pilotarea, doar pentru exterior

j. Mikado Logo 20

j. Mikado Logo 20

1. Serious aerobatics capable

2. Expensive (retail about $470)

3. About average durability

4. Manufacturer in Germany. Parts availability okay.

5. >3000 grams AUW, 1340mm rotor diameter, 20-24 cells

6. large, high headspeed, easy to learn hovering, outdoors only

- Capabil de acrobaţii avansate

- Costisitor (aprox 470 dolari)

- Durabilitate medie

- Made in Germany. Piesele se găsesc uşor

- >3000 grame AUW , diametru rotor 1340mm, 20+24 celule

- Turaţie ridicată, uşor de pilotat, doar pentru exterior

k. Robbe Eolo-R22

k. Robbe Eolo-R22

1. Moderate aerobatics capable

2. Expensive (retail about $300)

3. About average durability

4. Manufacturer in German?, parts availability okay

5. 1280g AUW, 810mm rotor diameter, 8 cells

6. large, high headspeed, easy to learn hovering, outdoors only

- Capabil de acrobaţii moderate

- Costisitor (aprox 300 dolari)

- Durabilitate ridicată

- Made in German. Piesele se găsesc uşor

- 1280 grame AUW, diametru rotor 810mm, 8 celule

Turaţie ridicată, uşor de învăţat pilotajul, doar pentru exterior

- 4. Recommended beginner configurations

4. Configuraţie recomandată pentru începători

These are configurations for beginners, and therefore we tend to

recommend inexpensive and mild setups rather than excessively

"hot" 3-D setups.

Note: Do not run R/C car-type "Speed 540" brushed motors (Atomic Force,

Fusion 7, etc) on more than 8 cells. Most R/C/ car motors are not

designed for more than 8 cells, and running them with more cells

will kill the motor after only a few flights.

a. Corona - brushed configuration

1. Kyosho Atomic Force brushed motor w/stock pinion

2. Castle Creations Pegasus 35H or 35P main ESC

(older Pegasus 35 has too high LVC)

3. 2 Hitec HS-85MGs for cyclic

4. 1 Hitec HS-81 for tail

5. Futaba GY240 HH gyro

6. 4 channel receiver

7. 7 or 8 cell SubC battery pack

b. Corona - brushless configuration

1. Mega Motors 16/15/3 brushless motor w/stock pinion

2. Castle Creations Phoenix 35 main ESC

3. 2 Hitec HS-85MGs for cyclic

4. 1 Hitec HS-81 for tail

5. Futaba GY240 HH gyro

6. 4 channel receiver

7. 7 or 8 cell SubC battery pack

c. FP Piccolo - brushed + Piccoboard

1. Stock Speed 295/310 motor

2. Piccoboard or Piccoboard Plus

3. 2 HS-50s (or HS-55s) for cyclic

4. GWS or Berg 4-channel receiver

5. 7 cell NiCad or NiMH battery pack

d. FP Piccolo - brushed - separates

1. Stock Speed 295/310 motor

2. 2 Castle Creations Pixie-7P main/tail ESC

(or GWS ICS-100E main and ICS-50E tail ESC)

3. 2 HS-50s (or HS-55s) for cyclic

4. Futaba GY240 or CSM HLG200 HH gyro

5. GWS or Berg 4-channel receiver

6. 7 cell NiCad or NiMH battery pack

e. FP Piccolo - brushless - separates

1. Hacker B20-36S brushless motor w/8 tooth pinion

2. Castle Creations Phoenix 10 main ESC

3. 2 HS-50s (or HS-55s) for cyclic

4. Pixie-7P or ICS-50E tail ESC

5. Futaba GY240 or CSM HLG200 HH gyro

6. GWS or Berg 4-channel receiver

7. 7 cell NiCad or NiMH battery pack

f. CP Piccolo or Pro - brushless - separates

1. Hacker B20-31S brushless motor w/8 tooth pinion

(for power) or

Hacker B20-36S brushless motor w/10 tooth pinion

(for duration)

2. Castle Creations Phoenix 10 main ESC

3. Pixie-7P or ICS-50E tail ESC

4. 2 HS-50s (or HS-55s) for cyclic

5. Futaba GY401 or CSM HLG200 HH gyro

6. GWS 6-channel receiver

7. 8 cell NiCad or NiMH battery pack

g. Logo 10 - brushless

1. Kontronik FUN 600-18 w/15 tooth pinion

2. Schulze Future 12.46e

3. 3 HS-85s for cyclic

4. HS-81 for tail

5. Futaba GY240 or GY401 HH gyro

6. 6 channel receiver

7. 12 cell NiCad battery pack

h. ECO 8 - brushed

1. Kyosho Magnetic Mayhem Reverse brushed motor

2. Castle Creations Pegasus 35

3. 3 HS-85MGs for cyclic

4. HS-81 for tail

5. Futaba GY240 or GY401 HH gyro

6. 6 channel receiver

7. 8 cell NiCad battery pack

(The MMR can run with 10 cells also)

i. ECO 8 - brushless

1. Hacker B50-18S or Mega Motor 22/20/3H motor

2. Schulze Future 12.46e

3. 3 HS-85MGs for cyclic

4. HS-81 for tail

5. Futaba GY240 or GY401 HH gyro

6. 6 channel receiver

7. 10 cell NiCad battery pack (will fly on 8 cells brushless,

but much better with 10 cells)

5. Brushless motor upgrade paths

You may want to choose a brushless motor which is usable in both

your first fixed pitch helicopter and your second collective pitch

helicopter. This is a little tricky but definitely possible if you

plan wisely.

In the following section, 10-12T means "10 tooth to 12 tooth pinion".

The lower tooth pinions are for duration, and the higher ones are

for power.

Corona upgrade paths:

There are three possible upgrade paths from the Corona: the ECO 8,

the Eolo, and the Voyager E. All of these helicopters can use 3.17mm

shaft motors in approximately the same Kv range as the Corona.

a. Corona motors usable in an ECO 8

This requires choosing a 3.17mm shaft motor with a Kv of about

2400-2600.  This results in a mild motor for the Corona, which

becomes a power motor when moved to the ECO 8 on 10 cells.

If you desire to use a Corona motor which will become a duration

ECO 8 motor, then you will need a motor with a lower Kv (about

2200-2400) and use a larger tooth pinion on the Corona.

A motor with 3000 Kv is usable on an ECO 8 with 8 cells, but

not really recommended for 10 cells.

Hacker C40-10L, Kv = 3000 rpm/V (Corona: 11-12T,

ECO 8 -  8 cells: 10T)

Hacker C40-12L, Kv = 2500 rpm/V (Corona: 12-13T,

ECO 8 -  8 cells: 12-14T

ECO 8 - 10 cells: 10-12T)

b. Corona motors usable in a Eolo

This requires choosing a 3.17mm shaft motor with a Kv of about 3300.

This results in a power motor for both the Corona and the Eolo.

The Mega 16/15/3 is fairly mild for both Corona and the Eolo.

Mega 16/15/3,   Kv = 3000 rpm/V (Corona: 10T, Eolo: ?)

Hacker C40-12S, Kv = 3500 rpm/V (Corona: 10T, Eolo: stock pinion)

Hacker C40-9L,  Kv = 3333 rpm/V (Corona: 10T, Eolo: stock pinion)

c. Corona motor usable in a Voyager E

This requires choosing a 3.17mm shaft motor with a Kv of about 3700.

This results in a power motor for both the Corona and the Voyager.

You must be careful to limit the throttle on the Corona because

the maximum headspeed of 2000 will be exceeded if the throttle is

not limited.

Hacker C40-8L, Kv = 3750 (Corona: 10T, Voyager: stock pinion)

Piccolo upgrade paths:

The FP Piccolo requires a motor with a Kv of about 2500.

There are two upgrade paths available: the Piccolo CP kit or the

Piccolo Pro, wich both require a motor with a Kv of about 3000.

The B20-31S and B20-18L have a Kv that's a little too high for

an FP Piccolo so the flight time will be short, but they will

be powerful later in a CP Piccolo.

B20-36S, Kv = 2500 (FP Piccolo: 8T, CP Piccolo: 10T)

B20-31S, Kv = 3000 (FP Piccolo: 8T, CP Piccolo: 8T)

B20-18L, Kv = 3000 (FP Piccolo: 8T, CP Piccolo: 8T)

6. Helicopter Parts Selection

a. Gyros

A heading hold gyro is highly recommended for beginners.

There are two reasons for this:

1. A heading hold gyro is much easier to configure than a yaw rate gyro.

The yaw rate gyro requires the revo mix curve to be set up correctly

before learning hovering, and this is tricky to set up for beginners.

(Exception: Piccolo heading hold module requires revo mix to be set)

2. The heading hold gyro will "lock" the tail at one heading rather

than just dampening random tail movement. This is very good because

you only need to learn two joystick axes initally instead of three.

This means you can learn the right joystick first, then learn

the left joystick later (for mode 2) instead of trying to learn

both joysticks simultaneously. This makes learning hovering much,

much, easier.

The GY240 is a very popular beginner gyro and is very easy to setup.

Also, the GY240 does not require a sensitivity channel and therefore

can be used with four-channel radios.

The GY401 is a more advanced gyro with many adjustment options.

It requires a dedicated channel for sensitivity adjustment so it is

not usable on a four-channel radio.

The CSM HLG200 seems to be more difficult to set up than the GY240

so is probably less suitable for beginners. In particular, it has

a tendency to drift left or right if not configured properly, which

will mean your helicopter will slowly change orientation which makes

hovering difficult.

The inexpensive Hobbico gyro is NOT recommended for beginners.

It is a yaw rate gyro, which makes hovering difficult for beginners.

Also, it is very fragile and there are many reports of it breaking

on the first heli crash from only 1.5 feet of altitude.

Some people have been using the FMA copilot on their first heli,

but I don't think this is really useful unless you are really having

problems learning hovering. A good heading hold gyro will help you

learn hovering more than an FMA copilot with a yaw rate gyro.

The Piccoboard used on the Piccolo is a single board with the following

items:

1. Yaw rate gyro (upgradeable to heading hold on the Piccoboard Plus)

2. Revo mixer

3. Main motor ESC

4. Tail motor ESC

5. BEC

The older versions of the Piccoboard had extremely fragile gyro

sensors and are not recommended for beginners. Supposedly the

recent ones are more durable. For more detailed information on the

various versions of the Piccoboard, consult Paul Goelz's Piccolo site.

The Piccoboard is not necessary for the Piccolo, and can be replaced

by either:

1. a standard gyro + two ESCs (w/BEC)

(requires revo mixing on transmitter)

2. a heading hold gyro + two ESCs (w/BEC) + transmitter

(no revo mix required on transmitter for this configuration)

Don't forget to disable one of the BECs on one of the ESCs.

b. Tail (rudder) servo

The tail servo for a helicopter needs to be very fast to respond

quickly to small random tail movements. The tail servo should have a

specification of 0.12 sec / 60 degrees of travel or better.

For the Corona, Logo 10, and ECO 8/16, some usable tail servos are:

1. Hitec HS-81

2. JR DS368			(do not use in DS mode, will burn out)

3. Volz Speed-Maxx XP		(DS mode compat,

will be released about Oct 2003)

4. Multiplex Micro BB Speed	(DS mode compat)

5. Hitec HS-5245MG		(DS mode compat)

The Multiplex Micro BB Speed is slightly larger than the HS-81/DS368

so some modification may be required to use it.

For the Logo 10 or larger, the Futaba S9253 is very popular used with

the GY401, although the S9253 is rather heavy for the Logo 10.

Some servo mounts will allow you to use high-speed micro servos for

the tail pitch servo, such as the Precision Model Products tail servo

mount for the ECO 8/16.

The metal gear servos are not recommended for the tail because the

metal gear servos wear faster and have more backlash than plastic gear

servos, which will result in less precise tail control (with the

exception of the Volz Speed-Maxx XP which is specifically designed for

tail pitch control)

The slower digital servos (such as the JR DS368, 0.21 sec/60 degrees)

do not work well as a tail servo unless the stock servo arms are

replaced by extra-long servo arms (Du-bro, Servo City, etc). This

sacrifices some precision for extra speed.

JR does not recommend the DS3421 for tail gyros because the servo motor

is too small to handle the frequent movement required.

Gyros are sensitive to temperature changes. If you car is warm, the

weather is cold and you take your heli out of the car and immediately

try to fly, the gyro will not work well. You should allow a few minutes

for the gyro temperature to settle before flying.

c. Swashplate (Cyclic) servos

Torque, speed, and precision should be considered for swashplate servos.

The Corona works fine on the stock HS-81 servos, although some people

choose to use the HS-85BBs for more torque.

The ECO 8/16 require a servo no taller than 1.1 inches, so this limits

servo choices considerably.

Corona/ECO 8/16 choices:

1. JR 341              (0.22 secs/60 degrees, 32 oz-in)

2. JR 351              (0.22 secs/60 degrees, 32 oz-in)

3. HS-81               (0.11 secs/60 degrees, 36 oz-in)

4. HS-85MG/BB+         (0.16 secs/60 degrees, 42 oz-in)

5. Volz Micro-Maxx     (0.16 secs/60 degrees, 55 oz-in)

6. Volz Micro-Maxx XP  (0.16 secs/60 degrees, 66 oz-in)

7. JR DS368

The Logo 10 uses servos from 1.1 inches to 1.3 inches tall, so

it can use all the servos used in the ECO 8/16 except the

servos with less torque are not suitable. Probably 42 oz-in of

torque is a reasonable minimum requirement for a Logo 10.

Logo 10 choices:

1. HS-85MG/BB+         (0.16 secs/60 degrees, 42 oz-in)

2. JR 341              (0.23 secs/60 degrees, 42 oz-in)

3. Futaba S3102        (0.25 secs/60 degrees, 51 oz-in)

4. JR DS368

5. Multiplex Micro BB?

I've been told the Volz servos are too deep to fit into the Logo 10

frame, so they are supposedly not usable for the Logo 10.

For the Piccolos, the most popular choices seem to be the Hitec HS-50

and the HS-55.

If you use ANY digital servos, see the BEC section for more info.

The HS-81s and HS-85BBs can be upgraded HS-81MGs and HS-85MGs by

replacing the plastic gears with the metal gears from the MG

version, which are available at many places (Servocity, etc).

d. Receiver

If you are using a gyro without remote sensitivity (like the GY240)

then you only need a five channel receiver with channels 1-4 and 6.

If your gyro has a remote sensitivity adjustment (like the GY401) then

you will need a six channel receiver with channels 1-6.

For a Piccolo you can use a Piccoboard instead.  The Piccoboard is a

tiny board with a yaw-rate gyro and two brushed ESCs, one for the

main motor and one for the tail motor.

The Piccoboard Plus is the same except it can be upgraded to

heading hold with a heading hold module. I haven't tried this, but

people have mentioned the GY240 works better than the HH module.

e. Motor

There are many, many motors available, but only a few are suitable

for each helicopter. This is because the rpm/V or the Kv of the motor

is very important due to the fixed gearing ratio of the drive system.

Motors are listed from mild to powerful. Please note that I have no

experience with most of these motors therefore the ordering should

only be considered a rough guide, and not absolute oracle. In general

the lower Kv motors with a larger pinion are milder and better for

duration flying, and the higher Kv motors with smaller pinions are

better for sport/aerobatic flying.

Be sure to use a heatsink on your motor. The neodymium magnets used

in most brushless motors will demagnetize if heated above 200 degrees

Fahrenheit. So, a heatsink is a very good idea to prevent your motor

from overheating.

The Hacker C40/C50 series is the same as the B40/B50 series except the

C40/C50 series has a built-in heatsink so no additional heatsink is

necesary. The Hacker B40/B50 series require an additional heatsink

available for $15.

The Mega 16/15/x series can use the Hacker B40 heatsink, and the

Mega 22/20/3H has a shaft extension for mounting a 5mm prop adapter

for cooling.

Most speed-540 size motors (36mm diameter) can use either the

Hacker B50 heatsink or a R/C car motor heatsink depending on

available clearance.

For more info on motors and pinion sizes, I recommend searching the

rcgroups electric helicopter and micro helicopter forums for people's

opinions on various motor and pinion combinations.

For the Corona:

Ideal Kv: 2700-3000 rpm/V

o Kyosho Atomic Force (brushed) mild

o Mega Motor ACn16/15/4 (brushless) mild

o Mega Motor ACn16/15/3 (brushless) mild

o Hacker C40-12S (brushless) powerful

o Astroflight 020 helicopter motor (4 turn) (brushless) ???

Note: All the brushless motors are good for duration in the Corona.

10+ minute flights are possible with careful power management.

For the FP Piccolo:

Ideal Kv: 1800-2000 rpm/V

o Astro Flight Astro 010 (brushless) mild

o Team Orion Modified Elite (brushed) powerful

o Hacker B20-36S (brushless) (8T pinion) powerful

o Model Motors ACn1215/20 (brushless) powerful

Note: The Astro 010 is very good for long flights.

For the CP Piccolo:

Ideal Kv: 2700-3000 rpm/V

o Hacker B20-36S (brushless) (10T pinion) mild

o Astro Flight Astro 010/14T (brushless) mild

o Team Orion Modified Elite (brushed) powerful

o Hacker B20-31S (brushless) (8T pinion) powerful

o Hacker B20-18L (brushless) (8T pinion) powerful

o Model Motors ACn1215/20 (brushless) powerful

o Astro Flight Astro 010/10T (brushless) powerful?

Note: The B20-36S is good for duration flights.

The B20-18L is good for aerobatics.

For the ECO 8:

Ideal Kv:

3.17 mm shaft motors: 2200-2600 rpm/V

5.00 mm shaft motors: 1600-2000 rpm/V

o Magnetic Mayhem (brushed) mild

o Hacker C40-13L (brushless) mild, good for duration

o Aveox 27/30/1.5 (brushless) ???

o Aveox 36/15/1.5 (brushless) ???

o Hacker C40-14S (brushless) mild

o Ikarus H8 (brushless) ???

o Hacker B50-18S (brushless) powerful

o Hacker B50-15L (brushless) powerful

o Hacker C40-10L (brushless) powerful

o Mega Motor ACn22/20/3H (brushless) powerful

o Kontronik 500-19 (brushless) powerful

o Hacker B50-13L (brushless) very powerful

o Lehner Basic 2400 XL (brushless) ???

o Lehner Basic 2800 XL (brushless) ???

o Hacker B50-11L (brushless) insanely powerful

(requires very good matched batteries)

Best value motor for ECO 8: Mega Motor ACn22/20/3H

Best overall motor for ECO 8: Hacker B50-15L

For the Logo 10:

5.00 mm shaft motors: 1800-2000 rpm/V

o Aveox 36/24/2 (brushless) ???

o Hacker B50-15L (brushless) mild

o Kontronik Fun 600-15 (brushless) powerful

o Hacker B50-13L (brushless) powerful

o Plettenberg Orbit 15-16 (brushless, 1070 rpm/V) ???

o Plettenberg Orbit 15-14 (brushless, 1220 rpm/V) ???

o Hacker B50-11L (brushless) super powerful

(requires very good matched batteries)

o Kontronik Fun 600-18 (brushless) very powerful

If you choose a brushless motor, then an autorotation gear is highly

recommended. Most brushless motors have extremely high torque so when

the motor spools down, the "braking" effect will be very strong. This

will very likely break the main gear teeth if you do not have an

autorotation gear. The only exception to this is the Corona; the

main gear on it is very tough and can handle a brushless motor

without an autorotation gear.

The older sensored Aveox motors (12xx and 14xx series) are only rated

to 20,000 rpm, and the JETI motors are only rated to 15,000 rpm.

You must be careful not to exceed these rotational speeds otherwise

the rotor may eject a magnet (e.g. "throw a magnet").

Therefore, I do not recommend these motors for helicopter use.

The better motors such as the newer Aveox, MEGAs, Hackers are typically

rated for 50k-70k rpm, which makes them a better choice for helicopter

applications.

The Modem Motors AXI series (outrunner) is not recommended. The motor

seems to have problems with the rotor wobbling and touching the stator

windings which burns out both the motor and the ESC.

The choice of a motor with a proper Kv for your helicopter is very

important, because most motor ESCs are not efficient when running

at much less than 90% throttle. If you run an ESC continuously

at low throttle, the ESC will probably overheat. Therefore, you

should select a motor + pinion combination that will allow the

motor ESC to run at 90-95% throttle for best efficiency.

Pole counts for motors are unfortunately difficult to find, and

are necessary to program some ESCs correctly. Here are the pole

counts that I have managed to find:

Hacker: 2 pole

Kontronik: 2 pole

Lehner: 2 pole

Mega 22/x/x: 6 pole

Plettenberg: 2, 4, and 6 pole

Also see Tohru Shimizu's helicopter brushless motor page at:

http://www.dokidoki.ne.jp/home2/tohrus/motorindexE.html

Check the length of your motor mounting screws before mounting!

If they go too deep into the motor they will short out a winding

which will damage the motor. Even worse, if you try to run a motor

with a shorted winding, it will burn out the ESC. So test the screw

length by screwing it into the motor with your fingers before

mounting in the frame.

f. Wire

(The Corona kit does not need extra wire if using the Fusion 35,

Pegasus 35, or Phoenix 35 controller)

The motor and battery wires are especially important on an electric

helicopter. If the wires are too then, then your helicopter will

have less power because power is lost overcoming the resistance of the

wire and the wire will become very hot.

For an Corona, ECOs, and Logos, you will need good quality 12-14 gauge

wire for the motor and battery leads. These wires will work well:

Castle Creations W13RB (13 gauge)

Astroflight wire       (13 gauge)

W.S. Dean's Ultra Wire (12 gauge)

Team Orion 12 gauge

The 12 gauge is very heavy and only recommended for extreme flying

and/or larger helicopters with high current draw (>30 amps). The

13 gauge wire should suffice for most types of flying.

For the Piccolos and Hornets, you will need good quality 20-22 gauge

wire for the motor and battery leads. This wire works well:

Castle Creations W20RB (20 gauge)

Sometimes wire is sold as "square mm cross-section" instead of AWG.

Here is a quick table for conversion:

1.5 sq. mm		15 AWG

2.5 sq. mm		13 AWG

4.0 sq. mm		11 AWG

g. Battery Connectors

Heavy-duty battery connectors are recommended to minimize power loss.

The following connectors work well for the Corona/ECO/Logo:

4mm gold-plated Corally "bullet" connectors

Astroflight "Zero-Loss" 50 amp connectors

W.S. Deans Ultra connectors

W.S. Deans micro connectors (micro helis)

JST BEC connectors (micro helis)

If you use the 4mm bullet connectors, you may want to use one male and

one female plug on the battery otherwise you may plug in the ESC

backwards, which will definitely damage it.

The Astroflight connectors are expensive but they are polarized and

of extremely high quality and highly recommended.

These connectors may have some problems:

Anderson's PowerPoles

Sermos Connectors

Tamiya connectors

The Tamiya connectors do not handle high current well. They will become

very, very hot when conducting large amounts of current.

Some people do use Powerpoles or Sermos with helis, but evidently some

ESC manufacturers are claiming these connectors have problems.

There has been a report of Schulze refusing to honor a controller

warranty due to the usage of Powerpole connectors.

Also, Rumrunner Hobbies' webpage states:

"Lehner/BK warrantee does NOT Warranty (and is not limited to):

...

If Sermos, Powerpole, or Tamyia style connectors are used in the

application."

Also mentioned:

"When connecting your new LMT controller to your batteries be sure

to use Deans style connectors or 4mm Gold connectors (gold connectors

are for racers only).  Other connectors such as Sermos, Powerpole,

and Tamiya connectors can NOT be used and WILL VOID your warrantee.

These style connectors have a tendency to arch (sic) and or spark as

your vehicle is in motion. They also have a much higher resistance

factor.  If the connector does arch (sic) during operation of your

vehicle it will short out the motherboard and render your controller

useless!"

h. ESC

In order to use an ESC for a helicopter, it needs to have the following

characteristics (or else have these functions programmable):

1. No brake

2. No reverse

3. Slow start-up

4. No low voltage cutoff or programmable very low voltage cutoff

(As low as possible, must be 0.7 volts/cell or less)

Most airplane ESCs are not suitable for helicopters because they

include a brake and have a fairly high low-voltage cutoff.

The JETI Micoprocessor (red label series) is not suitable for helis

because the throttle control is not smooth and is rather "steppy".

The Advance (blue label series) is supposedly better, but nobody

I know has tried this.

Some ESCs have an optocoupler (usually called OPTO) instead of a BEC.

The optocoupler electrically isolates the ESC from the control signal

which reduces the possibility of interference from the external BEC.

For the Piccolo, the following work:

Pixie-7P (brushed)

Schulze Future 11.20e (brushless, rather heavy)

Castle Creations Phoenix 10 (brushless, very light)

Piccoboard/Piccoboard Plus/Piccoboard Pro

For the Corona, the following work:

Castle Creations Pegasus 35 (brushed)

Castle Creations Phoenix 35 (brushless)

Hacker Master 40-3P (brushless, do not use the BEC on this ESC

because the ESC will overheat on 3 servos?)

For the ECO 8/16, the following work:

Schulze Future 12.46k

Schulze Future 18.46k

Hacker Master 40-3P Heli

For the Logo 10, the following work:

Kontronik Beat 55-6-18

Schulze Future 18.46K

Do not use the SMILE in the Logo 10 - it tends to burn out!!!

The Hacker Masters seem to burn out in the Logo 10 as well due

to ESD problems.

The Castle Creations Phoenix works fine in the Piccolos and the Corona

but does not work well in the ECO 8/Logo 10 and larger helis. The

current version of the firmware has a problem in two areas:

1) The soft start doesn't work properly. It will kick your heli

around 180 degrees and/or tip your heli over.

2) The governor mode doesn't work properly with a heading hold gyro.

The RPMs will go up and down even when hovering, which makes the

tail wag back and forth.

Therefore, the Phoenix is not suitable for larger helicopters until

these firmware bugs are fixed.

i. BEC (battery eliminator circuit)

If your heli uses up to 10 cells and uses only analog servos,

then you can use the BEC which is included on many ESCs such as

the Schulze Future 12.46k and the Castle Creations Phoenix 35.

If you are using more than 10 cells on a helicopter such as the

Logo 16/20 or ECO 16, then you must use a BEC which is designed for

more than 10 cells. Currently there is only one popular BEC, the

Kool Flight Systems Ultimate BEC. There are two models, one which

handles up to 29 cells and another which handles up to 36 cells.

If you are using any digital servos, then you will need to check the

ESC's onboard BEC amperage rating. Most ESC BECs are rated for only

1 or 1.5 amps which is insufficient to run a digital servo + 3 analog

servos. One digital servo with three regular servos can easily

draw well over one amp, so if your ESC's built-in BEC is rated for only

one amp, you will definitely need to use an external BEC.

If you use a one amp BEC with digital servos, it will probably overheat

during flight and shut down. This will cause you to lose control of

the helicopter and it will crash.

To use an external BEC with an ESC which already has a BEC, then you

will need to disable the built-in BEC of the ESC. To do this, check if

the ESC has one or two plugs which plug into the receiver.

If the ESC has two plugs (like the Schulze Future 12.46e), then one of

the plugs will have three wires and the other will have only two wires.

The plug with only two wires is the BEC plug. If you do not connect

this plug to the receiver, then the ESC's onboard BEC will be disabled.

If the ESC has only one plug (like the Castle Creations Phoenix series)

then the plug will have three wiresand the middle wire should be red.

Either pull this red wire out of the connector and tape it with

electrical tape to prevent it from touching other wires or use a servo

extension with the red wire pulled out and taped. This will disable

the onboard BEC of this type of ESC.

j. Batteries

Helicopters need batteries that can deliver high current. If you use

cheap batteries, your helicopter will likely not fly well.The Sanyo

CP2400 and RC2400s are the best choices for beginners on 1-2kg helis

because they are reasonably priced and can discharge at high rates.

NiMH batteries are usually higher capacity but deliver less current

than Nicad batteries, so they are better suited for duration flying.

The one exception is the Sanyo HR-SC which is a NiMH battery specially

built for high current drain which performs slightly better than the

CP2400/RC2400 (HR-SCs must be used immediately after charging for best

results).

NiMH batteries require about 5 charge/discharge cycles to reach full

capacity. They work best immediately after charging - if you allow

them to sit and cool off they will not work as well.

Both Nicad and NiMH battery packs should be slow-charged on the first

charge to ensure all cells in the pack will reach a full charge.

If this is not done, the cells in the pack may be at different states

of a charge and the pack may never fully charge properly.

If you notice a big drop in capacity in your battery packs after a

few months of use, this is probably due to the cells in the pack

having different states of charge. If this happens, you should try

to "rebalance" the cells in the pack by slow charging them at C/20 for

24 hours. This will usually restore the pack to full capacity.

This should only be done for Nicad and NiMH packs, and not for other

battery types such as Li-ion or LiPoly.

Your batteries will last much longer if you do not allow them to

become too hot, because the primary cause of battery failure is the

deterioration of the separator which is accelerated by higher

temperatures. Therefore, you should allow your battery packs to cool

a little after use before charging them again.

The batteries known to work well are:

(milliohms is a measure of internal resistance; LOWER IS BETTER)

Corona / Logo 10/16/20 / ECO 8/16:

Sanyo CP1700SCR		(NiCad 1700 maH, 5.5 milliohms)

Sanyo CP2400		(NiCad 2400 maH, 4.5 milliohms)

Sanyo RC2400		(NiCad 2400 maH, 3.2 milliohms)

Panasonic HHR300SCU	(NiMH  3000 maH)

Panasonic RC-3300HV	(NiMH  3300 maH, 5.0 milliohms)

Sanyo HR-SC		(NiMH  2600 maH, 4.0 milliohms)

Piccolo:

Sanyo HR-AAAU		(NiMH 720 maH, 30 milliohms)

PowerEx AAA NiMH

HECELL AAA NiMH

If you are buying batteries not on this list, then you should ask

the manufacturer for the internal resistance of the cells. If the

batteries do not have an internal resistance as low as the cells

on this list, then it is probably not suitable for helicopter use.

If you intend to fly aerobatics, do NOT use commercial battery packs.

Most of them use a flat springy metal to connect the battery terminals

and the springy metal will melt at high (50-60+) amps. Be sure to use

your own inline-soldered battery packs if you intend to do hard

aerobatics with your helicopter.

Lithium-polymer batteries are NOT recommended for helicopterbeginners.

They are fragile and incur damage easily, and when they are damaged

they can catch on FIRE up to ten minutes later.

`	There is a story on rcgroups where a guy crashed his plane with li-pos,

and put it in his SUV. Several minutes later someone told him his SUV

was on fire. He posted pictures of the totaled SUV, and the interior

was burnt to a crisp - it looked like a barbeque pit.

k. Mods

You should avoid adding any aftermarket modifications to the helicopter

when are are learning to hover. The reason for this is:

1. If you crash the helicopter, you may destroy your

expensive aftermarket modifications

2. You will be distracted by trying to avoid destroying your

expensive mods and therefore learn slower

The modifications to avoid when learning to hover are:

1. Carbon Fiber frames/crutches (cracks)

2. Aluminum frame upgrades (bends)

3. Aluminum head upgrades (bends)

Some mods are justifiable because they improve control and are less

likely to be damaged in a crash, such as:

1. Aluminum swashplate

2. Tail servo mount

3. Carbon fiber pushrod (only costs ~$3 to replace anyway)

4. Autorotation gear (REQUIRED for a brushless motor)

but in general, a stock helicopter is recommended.

7. Support Equipment

a. Pitch gauge

A pitch gauge is an absolute must for collective pitch helicopters.

It is unlikely you will be able to properly setup your non-micro

CP heli to hover without using a pitch gauge.

There isn't a good pitch gauge available for microhelis which makes

microheli trimming more difficult.

b. Blade balancer (optional)

If you don't buy a blade balancer, it is still possible to balance

the blades using a dowel or other method, but a good blade balancer

makes the job much easier.

The KSJ-528 blade balancer works well.  The Koll Rotor Pro is better

than the KSJ-528 but is overkill unless you're doing advanced flying.

I highly recommend CAing the tip of a sewing pin to the pointer of

the KSJ-528 to make the scale easier to read.

c. Paddle pitch gauge (optional)

This is very handy for ensuring your paddles are completely flat

relative to each other. For non-micro helicopters, the KSJ-624

paddle gauge works well.

d. Prop balancer (optional)

In order to balance the rotor head, you need a prop balancer.

The Du-bro "Tru-spin prop balancer" works well because you can

hang the rotor head over the edge of a table when balancing

the rotor head.

e. Tachometer

There are about three tachometers in wide use for helicopters.

The first is the Anderson Hobby tachometer. This is fairly cheap

(about $35) and works well on the ECO/Logo, but it does NOT work

on micro helis such as the Piccolo CP! It also drains batteries

quickly even when not turned on, so I recommend removing the

battery when not in use.

The second is the X-cell optical tachometer. This is expensive

(about $150) but works with almost any helicopter. It only reads to

1990 rpm, so it may not be suitable for micro helicopters which

typically need 2000+ rpm of headspeed.

The third is the Tera tachometer distributed by Thunder Tiger. This

is a very nice digital tachometer specifically for helicopters which

will clip onto the tail boom for hands-free measuring of the

headspeed.

There are other tachometers, including:

o Magnum mini-tach. Price is about $35.

o Hangar 9 micro digital tach

o Thunder Tiger 2642 mini tachometer

For some reason, Quantum Models (http://www.quantummodels.com)

stocks more tachometers than any other online store I've seen.

f. Ball link pliers

Ball link pliers are highly recommended for non-micro helicopters

because ball links are very difficult to remove properly without

ball link pliers. You do not need a ball link plier for micro

helicopters.

Both JR and Century make nice ball link pliers.

Be very careful when removing ball links on plastic balls

(such as the ECO 8/16 stock swashplate) with ball link pliers.

You can scratch deep grooves in the plastic balls if you fail to

center the ball in the jaws before squeezing.

g. Battery Chargers

There are many nice chargers on the market.

Here are the features I recommend you look for:

o For micros: able to charge at 500 ma - 1.5 amps

o For nonmicros: Able to charge at 3.5 to 5 amps

o Delta-peak charge termination

o Some type of false peak rejection capability

(Sometimes called soft-start, peak delay, etc)

The soft-start/false peak rejection capability is especially

important.  Helicopters tend to discharge cells rather deeply,

and when these cells are charged, the charger may often

"false peak detect". This occurs because the cell chemistry is

unstable when deeply discharged and the cell voltage will fluctuate

randomly until the cell chemistry stabilizes.

A charger with soft-start or false peak rejection will not require

restarting the charging cycle multiple times in the first 5-10

minutes of charging a deeply discharged battery pack.

The chargers which are known to fit these criteria are:

o Maha MH-C777 Plus II	(surface charge, Nicad, NiMH, Li-ion)

o Great Planes Triton	(peak delay, NiCad, NiMH, Li-ion, Pb)

o Hitec CG-330		(false peak reject, NiCad)

o Hitec CG-335		(false peak reject, NiCad)

o Hitec CG-340		(false peak reject, NiCad, NiMH)

o Robbe Infinity II		(false peak reject, NiCad, NiMH)

o Schulze ISL 6-330d	(false peak reject, NiCad, NiMH, Li-ion, Pb)

o Orbit Microlader		(soft-start, NiCad, NiMH, Li-ion, Pb)

o Orbit Microlader Pro	(soft-start, NiCad, NiMH, Li-ion, Pb)

Before buying a charger, make sure it can charge the number

of cells in your pack! Some chargers can only handle up to 10

or 12 cells, which is insufficient for a Logo 16/20 or ECO 16.

This may be important if you're planning on buying a larger

helicopter eventually.

h. Transmitter tray

A transmitter tray can help your helicopter flying skills. It holds

the transmitter at a natural angle which allows better control

of the joysticks. Petal Manufacturing makes nice transmitter tray

which works with most transmitter models.

8. Simulators

A simulator is highly recommended for helicopter beginners.

A typical well-trimmed helicopter will only hover in place for two

or three seconds "hands-off" before it starts to drift in a random

direction. Therefore, a helicopter requires constant correction to

hover in one spot. In addition, a drifting helicopter will gain

speed much like a ball rolling down a hill. If you are slow to

move the stick to correct the drift, then you need more input to

arrest the drift, so it is best to arrest the unwanted motion quickly

before it gains speed.

The hardest part of flying a helicopter is developing the "reflexes"

and the "delicate touch" necessary to instinctively correct the

drift quickly without overcorrecting. A simulator will help you develop

these skills quickly without spending a lot of money on replacement

parts.

Here is a quick subjective review of some simulators:

a. FMS - free! (score: 3/10)

FMS is okay for learning hovering in all orientations. The models

move extremely slowly so hovering is a little too easy. However, it

does not seem to model forward flight correctly, so once you are

ready to practice forward flight, I would recommend finding a better

simulator.

b. Piccofly with Game Commander - ~$80 (score: 7/10)

Piccofly is excellent for learning to fly the FP Piccolo. It doesn't

model forward flight well, but it simulates the "squirreliness" of

hovering the Piccolo very well.

It has a very nice "slow time" function which allows you to slow down

the movement of the Piccolo so you can build your reflexes withoout

getting too frustrated.

I would recommend starting off at about 70% time and gradually

increasing the time until you can hover at 100% time (real time).

c. Easyfly (included with Piccofly) (score: 4/10)

The quality of Easyflight's helicopter flight model is a little

better than FMS, but not by much. The helis move faster, which is

good, but forward flight doesn't feel right because there isn't

any translational lift. Okay for learning hovering, but not

forward flight.

d. Aerofly Professional - $130 to $200 (score: 5/10)

The helicopter flight model is a little bit better than Easyfly but

it still doesn't feel quite right. There's still not enough

translational lift, but at least it won't let you loop the

heli with 5 ft of altitude without negative collective like

Easyfly does. Good for learning hovering, but not forward flight.

e. Realflight G2 w/USB Interlink - ~$200 (score: 8/10)

Realflight G2 has a pretty good helicopter flight model, and is

a good simulator for learning non-micro helicopter skills.

The helicopter flight model is probably best of all the flight sims

mentioned here, and it will probably be good enough to practice

3D aerobatics.

I would recommend practicing hovering on the Impala model initially,

then later when you acquire proficiency I would recommend buying

the Add-ons 3 and practicing with the Raptor 30 model.

For some reason, many of the models in Realflight do NOT have the

heading hold function enabled nor the revo mixing set up correctly.

This means the helicopter will continually rotate and be difficult

to hover. If you have this problem, you should select "Copy Model"

and enable the heading hold gyro and also edit the radio to turn off

the revo mixing.

Basically, Realflight G2 is the only one which seems to simulate

helicopters properly. All other sims seem to model helicopters as

a special type of airplane, which does not produce the right

flight characteristics.

The incorrect translational lift model actually affects hovering

as well, because real (light) helicopters tend to bob up and down when

there is a slight wind. This is because the wind has the same effect

as forward flight - it makes the heli generate extra lift.

So, in Aerofly Professional, if you turn on wind, your heli doesn't

bob up and down properly - it just slides around horizontally, which

is incorrect. Realflight G2 models translational lift correctly, and

the heli will gently bob up and down as the wind gusts. It also seems

to model the "rotor wash" effect where the main rotor blades become

less efficient when they enter their own rotor wash.

Therefore, if you learn to hover completely in FMS, Easyfly, or

Piccofly, you will not learn how to properly use the collective

to compensate for the effect of wind making your heli bob up and down.

This can be learned later on a real heli, but it will require some

adjustment time.

Most simulators have wind turned off by default, which makes hovering

unrealistically easy. In order to accurately simulate being outside,

you should turn on a little bit of gusty wind (maybe 3 mph or so).

9. Transmitters

You can fly some helicopter with a simple four-channel radio, but you

will be limited to the following helicopters:

1. Piccolo with any Piccoboard

2. Hummingbird with onboard mixer board with any gyro

3. Corona with heading hold gyro with no remote gain (e.g. GY240)

4. ECO 8 with mechanical mixing with any gyro

Ideally, you want a better radio with at least six channels and some

or all of the following features:

a. No throttle detents ("notches")

Most airplane versions of radios have "clickers" which will only

allow a fixed number of throttle positions instead of a completely

linear throttle position. This is very annoying when flying helis

because the perfect throttle position for hovering is usually

between two throttle click positions so you wind up fiddling with

the throttle and bobbing up and down.

b. Exponential

This will allow you to make the helicopter cyclic less sensitive

around the center, which will help you learn hovering more quickly.

After you develop a delicate touch, you may want to reduce the

amount of exponential.

c. 5 point throttle/pitch curves (or better)

When flying a collective pitch helicopter, you will want a constant

headspeed from a little below hovering up to full throttle. This is

difficult to do with a three-point throttle pitch curve, and a

five point curve is better.

d. Throttle hold switch

This is a basic safety feature. It will prevent the helicopter from

spooling up if a gust of wind pushes your shirt over the throttle

stick or you accidentally bump it with your hand.

e. 90 and 120 CCPM swashplate support

Most helicopter nowadays use 90 or 120 CCPM swashplate modes.

If your transmitter does not support these modes, then you will not

be able to fly them.

f. Idle-up support

You will eventually want the capability to switch between two

throttle curves. One (normal) will be used to spool up the rotor

blades and the other (idle-up) will be used for normal flight.

Currently, the best price/performance in helicopter radios is the

Futaba 9CH (FF9 in Europe). This radio has all of the above features

and can be purchased for under $300 (without receiver/servos) at various

vendors on the Internet.

Other good choices which are moderately priced include:

JR XP8103 Heli (XP3810 in Europe)

Hitec Eclipse 7 Heli (can do 90 CCPM with programmable mixes -

see notes below)

Airtronics RD6000 Super Heli (do not buy the SPORT model because

the SPORT model has no swash mode)

These radios are very nice but are also very expensive:

JR 10X Heli

Futaba 9ZH

Airtronics RD8000 Heli

Hitec Eclipse 7 with 90 CCPM:

This is not supported directly by the transmitter, and must be done

using programmable mixes. This was taken from the Ikarus Forums:

Quick guide on how to set up your Hitec Eclipse 7 for the ECO 8 using

the stock 90 deg swash without the need for mechanical mixing.

First thing you need to do is set up your RX like this;-

Channel 1 - Aileron. Left servo on swashplate.

Channel 2 - Elevator. Rear servo on swashplate.

Channel 3 - Throttle. Goes to the ESC.

Channel 4 - Rudder. Tail servo.

Channel 6 - Pitch. Right servo on swashplate.

Now we move to the TX. Use the manual to set yourself up a 180 degree

swashplate helicopter.

OK, here is where we actually get the swash to work correctly.

If you turn you RX and TX on (engine disconnected please) and increase

and decrease the throttle you will see that the swashplate tilts back

and forth. This is not desired behavior. What we need to do is get

those pitch movements working on the servo on the back (Channel 2).

To do this we are going to use one of the Programmable Mixers on the

TX. To do this we have to enter "Programming Mode", it is done like

this;-

1. Make sure your ECO's battery is disconnected and your TX is on

(and your ECO is selected)

2. Hit the first two buttons at the same time on the bottom left (Edit

up and down, not Engine lock cut). The TX should now have something

like EPA 100% on it.

3. Hit the Edit up button (First button on the left) 6 times until you

see PMX1 inh (stands for Programmable Mixer 1 Inhibit).

4. Hit the Active/Inhibit button (Last button on the Right) the display

will change and have a lot of junk on it.

5. Select the Master Channel by hitting the Cursor Right button

(4th button).

6. Set the Master Channel to 6 by hitting the Data Increase button

5 times (5th Button).

7. Select the Slave Channel by hitting the Cursor Right button

(4th button).

8. Set the Slave Channel to 2 by hitting the Data Increase button once

(5th Button).

9. Select the Mix Ratio by hitting the Cursor Right button (4th button).

10. Select the Mix Ratio to 70% by hitting the Data Decrease button 30

times (6th Button, and you can just hold it down, you don't really

need to do it 30 times).

11. Turn on the mixer by switching the top right switch toward you.

The screen should now look like this;-

12. You're done!! Exit from Programming mode (first two buttons at the

same time on the bottom left) hook up your ECO (engine disconnected

still) and move the throttle, the swash should now move up and down

smoothly.

Some quick notes that may come in handy;-

You may need to reverse some servos.

Pitch and throttle curves must be setup now to complete the setup.

10. Helicopter Construction

General tips for all helicopters:

a. Do not rush building the helicopter. Take your time and be very

careful with everything, and make sure everything moves smoothly.

If all moving linkages do not move smoothly, then the helicopter

may have vibration problems later which will make hovering very

difficult. A few extra hours spent making sure linkages move

smoothly will pay off later when you shorten your hovering learning

time by a few months.

b. Only use threadlock on metal-to-metal areas. Do not use threadlock

on metal-to-plastic or plastic-to-plastic areas.

c. Blue threadlock is temporary, for stuff which may require disassembly

later (after a crash, etc). Red threadlock is permanent, for stuff

which will never be disassembled.

Example: Blue threadlock for a screw on a tail blade grip

Red threadlock for assembling the swashplate balls.

d. If your gears (including bevel gears and motor pinions) are meshing

together too tightly, you will lose a lot of power and your flights

will be very short. Make sure that the gear teeth only mesh

together by about 2/3rds to 3/4 of a tooth and there should be some

play. This will allow the gears to transfer power more efficiently.

This can be easily set by putting a plastic bag between the gears

and squeezing the gears together, then removing the bag.

e. When assembling a plastic frame with metal screws (e.g. ECO 8/16 and

Logo 10) be sure to use a jeweler's screwdriver or a Wiha with a

small handle to assemble the frame. If you use a large-handled

screwdriver you will not be able to "feel" when the screw is fully

inserted and you will probably strip the hole in the plastic frame.

f. If you strip a plastic screw hole, then you can fix it by squirting

a small bit of CA into the screw hole and letting it dry to give the

screw additional friction. But, it's better not to strip it in the

first place.

g. If you are using a brushed motor with carbon brushes, then you

should "break-in" the motor before your first flight. This break-in

procedure allow maximum contact of the brushes with the commutator.

This will allow the motor to run at maximum efficiency and extend

motor life.

(Break-in is not required for METAL (wiper) brushed motors. This

procedure is only for CARBON brushed motors.)

There are at least two ways to do this:

1. Dry method: Run the motor for two hours at 1/4 throttle.

2. Wet method: Run the motor for 10-15 minutes in a glass of water.

Be sure to disassemble the motor afterwards and throughly dry

everything, otherwise parts may rust. Don't use this method

on motors which are assembled using bent metal tabs (such as the

Piccolo motors) because the metal tab may break off when

disassembling or reassembling the motor.

Be careful with the carbon dust. It can get into your lungs and

cause severe breathing difficulty, especially if you're asthmatic.

Be sure to blow the carbon dust out OUTSIDE with some compressed

air and don't get the carbon dust into your lungs.

h. Beware of carbon fiber dust. It is classified as a hazardous

material and can cause severe breathing difficulty, especially

if you are asthmatic.

DO NOT CUT CARBON FIBER INDOORS. ALWAYS CUT CARBON FIBER OUTSIDE.

i. If you are using a brushed motor, be sure to solder three capacitors

to the motor: one between the positive terminal and negative

terminal, one between the postive terminal and case, and one between

the negative terminal and case. This will reduce the amount of

interference generated by the brushed motor.

j. If you are using a brushed motor, it may come with a diode which

you may need to attach to the motor. The diode looks like a black

barrel with a grey stripe on one side, and two leads coming out

each end.

This diode prevents ESC damage by shunting the spikes of reverse

current generated when the brushed motor rotates. So, you put the

diode on the power terminals of the brushed motor. The end with

the silver band goes on the postive terminal of the motor, and

the end with no band goes on the negative terminal of the motor.

k. Your ball links must move freely, but not be loose. If your ball

links are too tight, you can put the ball link on the ball and

gently squeeze around the edge of the ball link with a pair of

slip-joint or ball-link pliers.

If your ball links are too loose, then they can be tightened by

removing them from the ball then squeezing them gently across the

face of the ball link with a pair of slip-join or ball-link pliers.

l. For non-micro helicopters: If your motor output shaft does not have

a "flat" on the shaft, the pinion may spin around on the shaft

because the setscrew can't grip the shaft. To put a flat on the

shaft you need a Dremel with a diamond grinding tip, and a plastic

bag.

1. Put the motor in the plastic bag, then punch a hole in the

plastic with the motor shaft so the motor shaft sticks out the

bottom. Tie the back end of the plastic bag. This will prevent

metal shavings from falling into the motor and destroying it.

2. Grind a flat on the shaft using the Dremel.

3. Remove motor from plastic bag, being careful not to get any

metal shavings into the motor.

m. For the Piccolo: The stock plastic motor pinion may slip on the motor

shaft. We recommend using CA to glue the motor pinion onto the

motor shaft to prevent this from occuring.

n. For Futaba transmitters:

If you have only two servos controlling your swashplate (with

either non-CCPM or any CCPM) then the channel assignments are:

channel 1: left/right (roll) servo

channel 2: front/back (pitch) servo

channel 3: throttle (ESC)

channel 4: tail servo

channel 5: gyro sensitivity (optional)

o. For Futaba transmitters:

If you have three servos controlling your swashplate (either

non-CCPM or any CCPM) then the channel assignments are:

channel 1: left (roll) servo

channel 2: front/back (pitch) servo

channel 3: throttle (ESC)

channel 4: tail servo

channel 5: gyro sensitivity (optional)

channel 6: right (roll) servo

p. For JR transmitters:

If you have two servos controlling your swashplate (either

non-CCPM or any CCPM) then the channel assignments are:

channel 1: throttle (ESC)

channel 2: left/right (roll) servo

channel 3: front/back (pitch) servo

channel 4: tail servo

channel 5: gyro sensitivity (optional)

q. For JR transmitters:

If you have three servos controlling your swashplate (either

non-CCPM or any CCPM) then the channel assignments are:

channel 1: throttle (ESC)

channel 2: right (roll) servo

channel 3: front/back (pitch) servo

channel 4: tail servo

channel 5: gyro sensitivity (optional)

channel 6: left (roll) servo

r. Do not paint the canopy a dark color. You will need to focus

on the canopy while learning to hover, so be sure to paint

it a bright color or leave it white.

s. Do not use rubber servo grommets when mounting the tail servo

because this will cause tail wag when used with a heading hold

gyro.

Component Placement:

a. If you are using a brushed motor, the motor itself will be the

main source of RFI. Pragmatically speaking, you want to keep your

radio and gyro as far away from the brushed motor as possible.

This will eliminate and/or reduce the number of radio glitches.

b. If you are using a brushless motor, the ESC for the motor will be

the main source of RFI. So, it is desirable to locate the radio

and gyro as far away from the ESC as possible. On a Corona/ECO 8/

Logo 10, I would recommend at least two inches of spacing between

the ESC and the gyro/receiver.

c. Most gyros (GY240/GY401) require mounting on a horizontal surface,

but some gyros (Ikarus Profi, CSM HLG200, GWS PG-03) require

mounting on a vertical surface. Be sure to check your gyro's

documentation to see how it should be mounted on your heli!

d. Do not shorten any radio/servo wires until you have flown  a flight

or two and have checked for glitching strălucire.

Specific tips for LMH Corona only:

a. Many Corona kits seem to have missing parts. If you are missing a

part and you bought the kit directly from Lite Machines, call them

and explain your situation. If you bought from a retailer and not

Lite Machines, then talk to your retailer about the missing parts.

You may want to finish most of the model before reporting missing

parts so you don't need to call multiple times.

b. The general consensus on the Ezone regarding the Fusion-7 motor is

it's not very good. People have reported the motor dying after

as few as 5-10 flights. The Kyosho Atomic Force seems to be the

best alternative brushed motor. It is available from Tower Hobbies.

c. Make sure there is enough room between the two cyclic servos for

the servo arms to rotate freely without hitting the other servo.

If the servo arm rubs against the other servo, your front/back

cyclic control will be sluggish and hovering will be very difficult.

d. The manual recommends using one 4 dot blade grip and one 6

dot blade grip, but the heli is more stable and easier to hover

if you use two 4 dot blade grips because the headspeed is higher.

Later on if you want more lift you can switch one of the blade

grips to a 6 dot blade grip.

e. The labels on the main rotor blades seem to be attached using

the world's stickiest adhesive. The residue from the adhesive

can be easily removed using WD-40 or Goo Gone.

DO NOT USE ACETONE. ACETONE WILL MAKE THE BLADES BRITTLE.

IF YOU USE ACETONE, THE BLADES MAY SHATTER WHEN THEY HIT AN

OBJECT.

f. The Fusion 35 controller on the LMH Corona is a relabeled

Castle Creations Pegasus 35.

g. The Fusion 35/Pegasus 35 seems to have trouble arming on many

transmitters. If you turn on the transmitter, then turn on the

Corona and do not hear two beeps, then you are having this problem.

To fix this problem, you need to set a lower endpoint for the

throttle channel on your transmitter. For a Futaba 9C, go to

Menu->End Point->THR and set it to 125/125.

h. Many people make "tail boom protectors" to protect the tail boom

from boom strikes. This is usually foam wrapped around the tail boom

or a strip of 1/4" thick balsa or 3/8" dowel tie wrapped to the tail

to prevent the rotor blades from denting/bending the tail boom.

Other people use a "rotor deflector" which is a piece of wood or

angle aluminum mounted on the tail to deflect the rotor blade.

i. The feathering plate should be parallel to the swashplate. If these

are not parallel, then you may need to loosen the main shaft and

slide the main shaft down a little bit until the two are properly

parallel.

Specific tips for all Piccolo (Fun/ECO/CP upgrade/Pro):

a. Drill a hole through the landing skid (67361) so the struts (67378)

will go all the way through the skid. This will make the landing

skid much stronger. If you don't do this, then the nipple on the

landing skid will probably break off in a hard landing.

b. When building the landing skids (67361), use thick CA instead of the

thin CA included in the kit. The thin CA runs all over the place

and is difficult to get in the right place. Also, CA the rear

skid struts into the frame FIRST. Then CA the front skids into the

frame and make sure they almost align with the rear skid struts.

If you don't do this the landing skids will probably be crooked.

c. Do not use CA to glue in the tail boom. This usually works

too well. When you crash, it will be almost impossible to remove

all the tail boom bits and you will have to drill out the remaining

pieces. It is much better to put a few layers of CA on the ends

of the tail boom and let this dry throughly, then friction-fit the

tailboom into the body and the tail rotor assembly.

d. The landing skids may pop off the frame in even mild landings.

You can reinforce the landing gear by CAing a length of CF rod across

the front and rear landing gear skids about a half-inch (1.25cm)

below the chassis (67360). This absorbs most of the landing stress

that would normally pop the landing skid struts off the frame.

e. The Piccolo tends to lose the bearings on the hub (67566) on hard

crashes. You may want to purchase an aftermarket aluminum hub

or carefully thick CA the bearings to the stock hub to avoid losing

the bearings. Beware when purchasing an aluminum hub; some of them

appear to be made from soft aluminum and will bend easily.

I do not recommend J's aluminum hubs for this reason. The

Precision Model Products hubs are of much better quality.

Specific tips for fixed pitch Piccolo (ECO/Fun) only:

a. The stock Piccolo FP has excessive play in the control mechanism.

Specifically, the swashplate wobbles around too much. There are

two mods which are required to fix this: the ball-in-swash mod

and the Chris Rigoleth antirotation strap. These will make

your initial hover attempts somewhat easier.

b. The older FP Piccolo kits had a anti-rotation link (67366) with only

a single hinge rather than the newer double hinges. If you receive

a one of these single hinge anti-rotation links, they do not work

well, and I recommend you replace it with a newer double-hinge one.

Specific tips for collective pitch Piccolo (CP upgrade/Pro) only:

a. The pitch case (68211) will usually be too tight on the main rotor

shaft (68203). This will cause drag on the motor. To fix this, put

a 3mm drill bit into Dremel, then put the pitch case onto the

drill bit, then run the Dremel at low speed for about five minutes.

Hold the pitch case very gently to prevent it from spinning around.

After this, lubricate the inside of the pitch case with some

graphite to further reduce friction.

b. The M2x6 screw which holds in the pitch bellcranks (68212) will

usually rub against the flybar control levers (68209). To fix this

problem, put the M2x6 screws into a drill and hold the head of the

screw against a metal file to shave down the screw head. This will

prevent the screw head from rubbing against the flybar control lever.

c. Some CP upgrade kits include an older style flybar (68208) which

is not very good. The older style flybar is completely smooth

and does not have the grooves stamped into the flybar to prevent

the control arms (68209) and flybar paddle (67371) from slipping.

If you have one of these flybars, you should replace it, because it

will be almost impossible to prevent the control arms from slipping

on the older flybar even if you roughen the flybar.

Specific tips for Ikarus ECO 8/16 only:

If the ECO 8/16 is built strictly by the manual, you will create a

helicopter which has extremely tight linkages and will have severe

vibration problems and will be difficult to hover. Please follow these

tips so your ECO 8/16 will fly well.

a. It is possible make the ECO more durable and crash-resistant by

"doubling up" the sideframes. To do this, buy another set of

sideframes, and epoxy each set together - don't forget to rough

up the mating surfaces of the sideframes with 200 grit sandpaper

first for better epoxy adhesion. You will need replace the M2x8

with M2x10 screws, and also replace the M2x30 screws with two

extra-long M2 bolts or two M2 threaded rods because the M2x30s

will be too short to reach through the tail boom mounts. The

double frames will add about 41 grams to your AUW and reduce your

flight times by about 30 seconds, but the frame will be much

stiffer for better control and also survive most crashes.

b. The stock ECO 8 landing gear is a bit narrow and makes landing

difficult for beginners. You may want to replace it with the

ECO 16 landing gear (67916 + 67917) or the ECO 8/16 extra wide

landing gear (67822).

The ECO 16 landing gear is about 1 inch longer and two inches wider

than the stock ECO 8 landing gear. This landing gear will need

slight modifications to work on the ECO 8 because it is designed

to hold two battery packs.

The ECO 8/16 training gear is about 1 inch longer and 3.25 inches

wider than the stock ECO 8 landing gear. This can hold either one

or two battery packs and requires no modification.

c. The control balls on the plastic swashplate (67701) have been known

to break off on extremely hard crashes. You may want to upgrade to

the aluminum swashplate (67707) immediately. Also, the aluminum

swashplate can be configured to support 120 CCPM which offers better

control than 90 CCPM.

d. The stock main rotor shaft (67535), the stock feathering caracteristică shaft

(67509), and the stock tail rotor shaft (67550) are very soft and

bend easily in minor crashes.

If this happens, I highly recommend replacing them with the hardened

versions: 67940, 67942, and 67941 respectively.

e. I don't recommend using the mechanical mixer, because electronic

mixing works much better than the mechanical mixer. If you do

choose to use the mechanical mixer anyway, you will need fairly

strong servos because the mechanical mixer needs a lot of force

to move it around. Probably HS-81s are not adequate for mechanical

mixing - you need at least HS-85BBs.

f. The stock wooden main rotor blades are fairly durable and are

very good for beginners because they will survive minor crashes.

I would recommend using the stock wooden main rotor blades for as

long as possible - definitely while learning hovering in all

orientations.

g. Pg 6: The tail drive belt pulley (67702) may wobble because the

hole is not drilled exactly in the center of the pulley. This

usually does not cause problems, but in some cases the hole is

very out of center, and the tail belt may slap bate against the tail boom

as it spins up or while it's flying. In this case, it is advisable

to replace the tail belt pulley with a new one that is hopefully

better, or replace both ambele pulleys with the Voyager E rear belt

pulleys (060860), or replace both with aftermarket aluminum

pulleys (PMP ATPS).

h. Pg 8: If the aluminum skids (67563) are difficult to fit into the

undercarriage cross member (67562) try using a hairdryer to heat

the cross member until it softens slightly, then slide in the

aluminum skids.

i. Pg 9: When building the pitch compensator, the manual does not

mention the arm (67591) has a TAPERED ţuguiat hole for the pin. If you try to

force the pin through the narrow hole instead of the wide one,

this may cause damage to the arm.

j. Pg 9: The two collective pitch compensator arms (67591) will

rub against each other on a stock ECO, which is bad. You should

put an M2 washer between each arm (67591) and the hub (67590)

to increase the spacing between the arms.

k. Pg 10: The flybar seesaw leagăn (67610) usually does not seesaw smoothly

on the rotor center unit (67639). This flybar seesaw needs to

move very smoothly on its pivots otherwise this will cause

vibrations when hovering.

To fix this problem, take some extra-fine steel wool lână (#000) and

spread răsfira it with your fingers to make a very thin mesh. This mesh

should be about 1 inch by 1 inch and be mostly mai ales air with about

50 or 60 strands of steel wool running through it.

Remove the flybar seesaw, then put the steel wool mesh on top of

the pivot, then mash the seesaw on top of it so the steel wool is

trapped between the pivot and the seesaw. The seesaw should snap

on with moderate pressure; if you need too much pressure then

your steel wool mesh is too thick.

Now wiggle the seesaw up and down about 10 times, then remove the

steel wool and check if the seesaw pivots smoothly. If it still

does not pivoty smoothly, then repeat this process. Do not repeat

more than twice because this will wear out the pivot.

For the final finish, apply some powdered graphite onto the pivot.

After this, the seesaw should move very smoothly.

l. Pg 10: The flybar (67609) usually does not rotate smoothly in the

flybar seesaw (67610). You MUST make the flybar seesaw rotate

smoothly in the flybar seesaw otherwise the heli will be very

difficult to hover. You will need to push the flybar through the

flybar seesaw repeatedly (like playing a violin) for about 5 minutes

until the rod slides smoothly through the flybar seesaw. This will

make the heli much more stable and easier to hover.

m. Pg 11/update: (Advanced) You can give make a free tail pitch slider

upgrade by installing a brass ball on the outer slide ring (67643).

You must do this modification BEFORE the needle bearing (67644)

is installed inside the outer slide ring.

Cut off the plastic ball from the outer slide ring, then drill a

1.5 mm hole where it was. Take an M2x8 screw and a brass ball,

and screw it into the 1.5 mm hole. Look inside the outer slide

ring and check how much of the screw protrudes inside. Remove the

screw and trim it to size, then CA the screw and brass ball into

the outer slide ring.

n. Pg 13: The tail blade grips (67542) should controlled by the

leading principala edge margine of the blade, and not the trailing deschizător edge. If the tail

blade pitch is controlled by the trailing edge, the tail may wag a da (din coadă);.

Double-check and make sure the Ikarus logo on the tail blades

is visible from the right side of the heli, and the control ball

for the tail blade grips is on the leading edge of the blade.

o. Pg 13: There is a serious problem on this page. In some versions of

the English manual, the instructions do not mention using threadlock

on the screw holding the tail blade grip (67603) to the tail hub

(67549). The German version of the manual correctly tells you to

use threadlock on this screw. If you fail to do this your tail rotor

grip may fall apart in flight causing the heli to pirouette out

of control. Do not skip the threadlock on this screw! Also, if you

disassemble and reassemble the tail rotor later, don't forget to

reapply fresh threadlock on this screw!!

Also, be sure the screw tail blade grip is left slightly loose so

it can rotate freely on the ball bearing and screw. If the tail

blade grip is screwed too tightly to the tail rotor hub, then the

tail may "wag" because the mechanics may bind and gyro will have

trouble controlling the tail blade pitch.

One popular mod for this is the "double ball bearing mod" - this

involves using two 2x6x3 ball bearings in each blade grip (instead

of just one per blade grip) and substituting a M2x8 screw instead.

This reduces slop oblic significantly in the tail and is highly

recommended.

p. Pg 13: The M2x6 screw (67561) should not be screwed too tightly

into the short ballend (67564) on the tail. If the screws are too

tight, then the tail pitch lever will not move smoothly around

the middle of its range because the ballends will not be free

to flex outwards. To adjust this screw properly, screw it in

completely, then reverse it approximately one-eighth turn.

This should be about right but you should check the pitch lever

movement to verify it moves smoothly.

q. Pg 13: The pitch lever (67541) must move VERY freely on the tail

housing (67548). On an unmodified ECO this is very sticky, which will

make the tail "wag" with a heading hold gyro!

To fix the stickiness problem, rub the post where the pitch lever

mounts with some extra fine steel wool to remove the grooves left

from the molding process.  Next, apply some powdered graphite to the

post and to the inside of the pitch lever and mount the pitch lever.

Wiggle the pitch lever a few dozen times to spread the graphite.

The pitch lever should now move very smoothly.

r. Pp 16-21: Don't use servo grommets to mount the servos to the frame.

Instead, cut a 4mm length of very small fuel tubing and slide this

onto the M2 screw. When this tubing is compressed, it will fatten

out and fill the gap between the servo and screw.

s. Pp 16-21: If you are using the aluminum swashplate with 120 CCPM,

mount one servo in front and two in the back at the 12 o'clock,

4 o'clock, and 8 o'clock positions. This is easier to mount than two

servos in front and one in back. You will need to fiddle with the

transmitter swashplate setting to swap the front and back with

this servo configuration (SWASH AFR on the Futaba 9C).

Note: This servo arrangement will not work with a frame brace

(because the front servo will hit the frame brace) nor will

it work with a stock Hacker B50 heatsink (because the heatsink

will hit the frame brace). The Hacker B50 heatsink will

require about a 1.25" section of it removed so it doesn't

interfere with the front servo.

t. Pg 22: The suggested component placement will work if your gyro

requires mounting on a vertical surface but does not work well

if using a gyro which requires mounting on a horizontal surface

such as a Futaba GY240 or GY401. If using these gyros, then mount

the gyro on top of the tail boom support behind the shaft (instead

of the receiver) and mount the receiver upside down under the tail

boom support (where the frame is angled). This component placement

keeps the ESC far away from the receiver and gyro and prevents

radio glitching problems.

Specific tips for Logo 10 only:

a. See http://www.logoheli.com for excellent construction tips

b. Some Logo 10 kits are missing parts and/or including the wrong

sized ball links. If your kit has this problem, you should contact

the retailer who sold you the kit and explain your problem.

c. Many Logo 10 owners have reported the tail belt builds up static

electricity in the tail boom. This can cause glitching and/or

ESC failure. Extreme care must be taken with component placement.

Specific tips for the Gensmantel Micro Heaven:

a. The pulley/shaft assembly for the tail may have the pulley either

too low or too high. This can be fixed by putting the shaft/pulley

on a vise and gently tapping the shaft through the pulley.

b. The tail boom mount screws will hit the frame. You may want to

countersink the tail boom mount screws to avoid this.

c. When the 3D main rotor shaft support is installed, the main rotor

shaft may bind. Make sure the main rotor shaft still turns freely

after you install the main rotor shaft support.

11. Soldering technique

Good solder joints are extremely important for an electric helicopter.

Electric helicopters require extremely large amounts of current for

even simple acts such as basic hovering.

If the battery and motor connections are not soldered correctly, then

the motor may not receive enough current and the helicopter may lack

power to fly properly.

The basic steps to forming a good solder joint are:

1. Select the correct size soldering iron for the application

If you are soldering small wires (about 20 gauge) then you should

use about a 20 watt soldering iron. If you are soldering battery packs

or larger wires then you need at least a 40 watt soldering gun to

have sufficient heat to solder properly.

2. Use the correct solder

You need ROSIN core solder for soldering electrical connections.

Do not use acid core solder, because this solder is for applications

such as plumbing and the acid will cause corrode the wires and

connectors.

3. Allow the soldering iron/gun to warm up

It requires approximately 750 degrees Fahrenheit to melt solder.

If you try to solder before the iron/gun is fully heated, then

the solder will not melt properly.

If the soldering gun does not heat up properly and/or takes too

long to heat, then the screws holding the tip have probably

loosened, so not enough current is flowing to the tip. Disconnect

the soldering gun then tighten the screws.

4. Clean the surfaces to be soldered if necessary

If you are soldering batteries together you will need to clean

the surfaces with some sandpaper before soldering.

This is not required for gold- or zinc-plated connectors or

circuit boards which are already coated with solder, or for wires

which have recently been stripped.

5. Twist the wire conductors tightly together

If they conductors of the wire are loosely twisted then they will

not heat properly and it will be very difficult to solder them.

If you apply a little extra twist just before soldering, they will

be much easier to solder.

6. Coat ("tin") the mating surfaces with solder

(do not solder them together yet)

If soldering wire to a gold-plated bullet connector or an

Astroflight Zero-Loss connector, then do not tin the connector.

This involves two steps:

a. Touch the soldering iron to the surface to heat it

b. Touch the solder to the surface and let the solder melt

A common mistake is to apply the solder directly to the soldering

iron/gun tip. This is not the correct way to solder and will create

a hole in the soldering iron/gun tip after a while. The solder shoud

be touched to the surface to be tinned. If it does not melt, then

the surface is not hot enough.

7. Touch the parts together then heat with a soldering iron

This step is much easier if you clamp one of the parts with a small

table vise to keep it from moving, and hold the other part with

a wooden clothespin to avoid burning your fingers.

Alternatively, you can drill a hole in a block of wood to hold

bullet or Zero Loss connectors while soldering.

When the the soldering iron is touched to the solder it should

melt and merge with the solder on the other surface. After the

solder has completely melted, remove the soldering iron tip and

let the solder cool. Be sure not to move the parts while the

solder is cooling.

8. Visually inspect the soldering joint

The solder joint should be smooth and shiny after the solder cools.

If the solder joint looks dull and grainy, then the solder joint

is bad and it should be reheated to let the solder flow properly.

You may need to apply a little fresh solder so the fresh rosin

will allow the solder to flow freely.

9. Be sure to WASH YOUR HANDS after soldering

Most commercial solder is 60% tin and 40% lead. Lead is harmful

to your body and causes lead poisoning which prevents calcium,

iron, zinc and other minerals from being properly used by your body.

Be sure to wash your hands after soldering before eating!!!

12. Basic setup

a. Balancing the heli - forward/aft

The lengthwise CG of a helicopter should be at its main

rotor shaft or slightly forward. Otherwise, the heli will have

a tendency to drift forwards or backwards.

To check this, first install the heli's batteries where

you think they should go. rotate the main rotor so the blades

are perpendicular to the body. Grab the main rotor blade grip

closet to you and raise the heli up to eye level.  Now find

a wall corner or door jamb, and move the heli around so you

can see the vertical line of the wall corner behind the

helicopter.

Now try to align the main shaft with the vertical line.

If the main shaft aligns perfectly with the line, then

no adjustment is necessary. If the nose is light, then

you will need to pull the battery pack forward. If

the nose is heavy, then pull the battery pack backwards.

Repeat until you find the correct battery position

to balance the heli correctly.

If you use a tail servo mount on the ECO, the battery pack will

need to be shifted forward quite a bit to adjust the CG

properly. If you do this, you will need to put a rubber band

over the two front side frame pegs to support the battery pack.

b. Balancing the main rotor blades using the KSJ-528 blade balancer

This step is not necessary for the Corona because the

blades are balanced while building (great manual).

Balancing the blades will minimize vibration which will

make hovering easier, and it will give the heli more power

because less energy is wasted shaking the heli.

Also the heading hold gyros will work much better with less

vibration because they gradually accumulate yaw error with

every little motion. Reducing vibruation will minimize the

"gyro drift" where the heli slowly starts to turn.

Therefore, balancing the main rotor blades is very, very

impoortant.

There are multiple ways to balance the blades, but this method

works best for me so far. It minimizes the amount of tape used

and we avoid disrupting the airflow where the blades generate

the most lift by putting most of the tape near the bolt holes

and the CG.

Be sure to use ELECTRICAL tape to balance the blades. Regular

transparent tape is not heavy enough. Electrical tape weighs

about 0.1 gram per 2.5cm (1 inch).

Step one: Matching the CG

1. Remove the blade holder posts from the balancing

tray of the KSJ-528.

2. Make sure the balancing tray balances evenly when nothing

is on the tray. If necessary, use the setscrews to balance

the tray.

3. Place one blade in the KSJ-528 tray and delicately shift

the blade left or right across the balancing tray until

the blade balances.

4. Mark this point with a felt tip pen.

5. Repeat for the other blade.

6. Place the two blades next to each other and check if the

CG of the blades match within 1/16th of an inch.

7. If the CGs are close enough, go to Step two: Matching weight

8. Determine which blade has CG farthest away from the mounting

bolt hole.

9. Move the CG of this blade closer to the bolt hole by placing

placing 1-2 inches of electrical tape on the underside of

the blade next to the leading edge near the bolt hole.

10. Measure the CG on this blade again and mark it.

11. Go to step 6

Step two: Matching the weight

1. Determine which of the blade holder posts fit your blades,

then mount them on the balancing tray.

2. Make sure the balancing tray balances evenly when nothing

is on the tray. If necessary, use the setscrews to balance

the tray.

3. Mount the blades on the blade holder posts and make sure

both blades balance and are perfectly horizontal.

4. If the blades do not balance, put a small strip of

electrical tape on the underside of the lighter blade at

the CG point next to the leading edge of the blade.

5. Add or remove tape on the lighter blade at the CG point

until the blades balance.

Step three: Optimizing tape usage (optional)

1. If only one blade has tape or you used less than seven

inches of tape in steps one and two, you can skip this

step.

2. If one blade has a lot of tape near the bolt hole and the

other blade has a lot of tape on the CG, then you should

definitely perform this step.

3. On the blade with tape near the bolt hole, remove all the

the tape.

4. On the blade with tape at the CG, remove the tape and discard

half of the tape. Reapply the other half of the tape to

the blade but at a point halfway between the CG and the tip.

5. Go back to step one and rebalance. The blades should require

less tape to balance this time.

c. Transmitter Throttle setup

1. If you are using a Futaba transmitter then you will need to

reverse the throttle servo direction.

2. Remove the main rotor blades temporarily so you can check

the spin direction of the rotor head.

3. Install a battery in your heli, then follow the ESC

directions to arm the ESC.

4. Give just enough throttle on your transmitter to

make the head spin a little.

5. If you have a brushed motor and your main rotor blades are

spinning backwards, then you need to reverse the motor

rotation direction. Swap the two wires connected to

the motor. If you have a diode wired to your motor,

be sure to swap this also so the grey band is still on the

positive terminal of the motor.

6. If you have a brushless motor and your main rotor blades

are spinning backwards, then you need to reverse the motor

rotation direction. To do this, swap any two of the three

wires connected to the motor.

d. Transmitter Swashplate setup

For the Hitec Eclipse 7 using 90 CCPM, see the special note in

the transmitter section.

If using 90 or 120 CCPM:

1. First, set the correct swashplate type in your transmitter.

You wil prbably need to consult your transmitter manual to

select the correct swashplate configuration for your

transmitter.

2. Disconnect the motor. Make sure the ESC motor leads cannot

touch together because if they touch during testing, you

will probably destroy the ESC. Put electrical tape on the

ESC motor leads if necessary to ensure they don't touch.

3. Move the throttle up on the transmitter, and make sure

all the servos move the swashplate UP. Move the throttle

down and make sure the swashplate moves DOWN.

If this doesn't work and some servos are moving in the

wrong direction, reverse the direction of those servos

until the swashplate moves up and down correctly.

For transmitter mode 2 (US):

4. Move the RIGHT transmitter stick up and down. This should

move the swashplate forwards and backwards.

Move the RIGHT transmitter stick left and right. This

should move the swashplate left and right.

For transmitter mode 1 (Asia and Europe)

4. Move the LEFT transmitter stick up and down. This should

move the swashplate forwards and backwards.

Move the RIGHT transmitter stick left and right. This

should move the swashplate left and right.

If any of these swashplate movements are reversed, then use the

SWASHPLATE AFR function (on a Futaba 9C) and change the aileron

or elevator from +50% to -50% to fix the swashplate movement.

Also, ensure that the servos do not bind at the minimum/maximum

servo positions. The servo binding draws a lot of power which

may cause the BEC to overheat and shut down, which will cause

the receiver to stop working, which will cause the helicopter

to crash. Therefore, if binding is observed, you will need to

adjust the servo endpoints on your transmitter to limit the

servo movement to eliminate the binding.

When the sticks are centered, the swashplate should be level.

The easiest way to check this is by holding the helicopter

at eye level, then looking at a bookcase behind it.

Align the main shaft with the edge of the bookshelf, then

raise/lower the helicopter until the swashplate is at the

same level as one of the shelves. You should be able to

easily tell if the swashplate is perfectly level or not.

e. Swashplate leveling

Temporarily disconnect the ESC wires from the motor.

Insulate them with electrical tape if necessary to prevent

them from touching each other.

Turn on the transmitter then power up the helicopter.

Remove any transmitter trim from the cyclic controls.

Now check the following items:

Servo centering:

Check to make sure the cyclic servos are all in the middle

of their travel range. For most helicopters this means

the servo arm should be perpendicular to the servo body.

If the servo arm is not centered,  then unscrew the servo

arm from the servo and remount it so the arm is perfectly

perpendicular to the servo body.

Swashplate leveling:

Once the servo centering has been set, the swashplate

should be perfectly level with the floor. There should

be no tilt to the left/right or forwards/backwards.

If the swashplate is not perfectly level, then remove

and adjust the length of the linkages from the servos

to the swashplate until the swashplate is perfectly level

when the cyclic servos are centered.

f. Flybar paddle setup

This step is not necessary for the Corona since it is already

performed by the instructions in the construction manual.

The tilt of the flybar paddles needs to match the tilt of

the swashplate. This is done by adjusting one flybar paddle

at a time.

First, make sure the flybar paddles are parallel to each other.

This can be done using the KSJ-624 paddle gauge or just by

visual inspection. If the paddles are not parallel to each

other then loosen the paddle mounting screw or setscrew

and twist the paddle and retighten the screw.

Next, rotate the main rotor so the main rotor blades are

aligned with the body, e.g. one points forward and the other

points backwards.

Pick one flybar paddle, and lower it slightly so it almost

obscures the swashplate. Now align the outer edge of the

flybar paddle with the top of the swashplate. It should

be level with the top of the swashplate.

If the paddle is tilted relative to the swashplate, then

this should be fixed by shortening or lengthening the linkages

between the swashplate and the flybar paddles

Now rotate the rotor head 90 degrees so the flybar paddles

are aligned with the body. Check the same paddle against

the top of the swashplate again. It should still be aligned.

Repeat the last two steps for the other flybar paddle

and make sure it is aligned with the top of the swashplate

at two different angles 90 degrees apart.

g. Transmitter Exponential setup

The "exponential" can be used to increase or decrease

the servo movement around the stick center.

For a helicopter, you want to decrease the servo movement

around the stick center so you can make smaller corrections

when hovering.

For the Futaba radios, I would recommend a setting of -20%

to start.

For JR radios, this value is reversed, so set this to 20%.

h. ESC programming

If you are using a programmable ESC which uses the transmitter

to set the ESC options and you have previously set a throttle

curve for this model, then you may need to reset the throttle

curve to default (e.g. linear from 0 to 100%) to program the

ESC otherwise the ESC may not be able to recognize the

low-middle-high stick positions.

For the Castle Creations ESCs, the following

parameters should be used:

1. Cutoff Voltage: as low as possible so the heli

will not fall out of the sky.

2. Current Limiting: insensitive

3. Brake: disabled - so we don't strip the main gear

4. Throttle Type:

For FP helis: fixed endpoint

For CP helis: high RPM governor mode

5. Timing Advance: depends on motor, choose standard if unknown

6. Cutoff: soft

7. PWM Switching Rate: depends on motor, but 11 khz is fine for

most motors (except Kontronik Samba needs high switching

frequency)

For other ESCs, set the parameters using the above parameters

as a general guide.

If you have a programmable ESC which is programmed using beeps

then you should carefully watch the tail servo when the ESC

beeps. If your tail servo wiggles every time the ESC beeps,

then your gyro or gyro wires are too close to the ESC.

i. Transmitter Throttle Curve setup

For a fixed pitch heli the throttle curve should be left as

default - linear from 0 to 100%. It is not necessary to check

the headspeed because you are unlikely to exceed the maximum

headspeed, as the heli will take off like a rocket if the

headspeed is too high.

For a collective pitch heli you should get a tachometer to

measure the headspeed. Borrow one from a friend if necessary.

For the next step, you will need to know your desired

head speed.

Hornet CP:      2000-2200 rpm

Piccolo CP/Pro: 2000-2200 rpm

ECO 8		1400-1800 rpm

Logo 10		1800-1900 rpm

Most microhelis will have a nasty wobble below 1800 rpm, and

most nonmicro helis will have a nasty wobble below 1400 rpm.

If you can't reach the proper head speed, you should buy a

new pinion with the proper number of teeth before proceeding.

With a collective pitch heli with a five point curve on the

transmitter, it should be set to roughly 0-50-x-x-x where x is

the throttle position at which you have the desired headspeed.

For a collective pitch heli with a three point curve on the

transmitter, it should be set to  0-x-x where x is the throttle

position for the desired headspeed.

If x is not between 80% and 90% of throttle, you should select

a different sized motor pinion because the motor will not be

running efficiently which will decrease your power and

flight time.

Note: If you have a Futaba radio and a Fusion 35 ESC, then

you may have problems properly arming the ESC. If you

have this problem, then try increasing the throttle range

to 125% so the low endpoint is lower.

j. Transmitter Throttle Hold setup

You should follow the transmitter manual directions to enable

the throttle hold function on your transmitter.

Throttle hold is very good because it prevents the heli from

throttling up if you must work on the heli while it's powered

and something bumps the joysticks.

k. Tail rotor pitch servo setup

1. If your tail rotor is on the right side of the boom and

you push the rudder right, the tail blades should increase

in pitch.

2. If your tail rotor is on the left side of the boom and

you push the transmitter rudder left, the tail blades

should increase in pitch.

The tail pitch control servo should be able to move the tail

pitch control lever all the way from one limit to the other

with about 150 degrees of servo arm travel.

If the servo needs more than 150 degrees of travel to reach

both limits of the pitch control lever, then replace the

servo arm with a longer one.

If the servo needs considerably less than 150 degrees of travel

to reach bot limits of the pitch control lever, then move

the servo arm linkage to a hole closer to the servo arm pivot

then check again.

The tail servo should be in the middle of its travel range

when the tail pitch lever is also in the middle of its travel

range. If this is not true, then adjust the linkages until

the midpoints are matched.

l. Gyro setup

Heading Hold Gyro setup:

First, if you are using a heading hold gyro (such as the GY240

or GY401) you must make sure your transmitter REVO MIXING option

is disabled, because this option is only for non-heading hold

gyros.

If you are using a Piccoboard with a heading hold module, you

do not need to trim the helicopter properly without the

heading hold module installed (e.g. as a yaw rate gyro).

Just install the heading hold module and it should work

properly as a heading hold gyro. You may need to adjust

the gain however.

GY240 setup:

There are three controls which require setup on the GY240.

Setting AVCS:

Set to ON. You want heading hold enabled.

Setting DIR:

Turn on the transmitter.

Disconnect the heli motor.

Plug in the heli battery.

Wait for the gyro to initialize.

Turn the heli right about 20 degrees. If your tail rotor

faces left (Corona) then the tail rotor blades should

increase in pitch. If your tail rotor faces right

(ECO, Logo) then the tail rotor blades should decrease

in pitch.

If the tail rotor blade pitch change is wrong, then flip

the direction switch on the gyro, and retest.

Setting GAIN:

For the Corona, the GY240 does not hold the tail well

without high gain, so set this to about 75%.

Otherwise, set this to 50% to start. It can be adjusted

later if the tail wags too much.

GY401 setup:

There are five controls on the gyro and one on the

transmitter which require setup on the GY401.

Setting DS:

This should be OFF unless you are using a S9253

S9250, S9450, etc digital servo compatible with

a fast update rate. Not all digital servos are

compatible with the GY401 DS mode!

Setting DIR:

See the GY240 section on setting this switch.

Setting DELAY:

Set this to about 50 initially.

If your tail servo is fast (<0.11 sec/60 degrees) set

this to a lower value.

If your tail servo is slower or you are using a fixed

pitch tail driven by a variable speed motor (Piccolo,

Hummingbird, etc) then set this to a higher value.

Setting LIMIT:

This controls the amount of tail servo travel.

Turn on the transmitter.

Disconnect the heli motor.

Plug in the heli battery.

Wait for the gyro to initialize.

After the gyro has initialized, make sure the tail

servo is at the center of its travel range (90 degrees

to servo body) and the tail pitch lever is at the

center of its travel range as well (90 degrees to

tail boom).

Turn off the AVCS mode temporarily at the transmitter.

Use the rudder stick and give full left rudder and

full right rudder. The tail servo should be moving

moving the tail pitch slider through its full range

of motion.

If the tail pitch slider is not moving far enough,

then you will need to increase the LIMIT control.

If the tail pitch slider is moving too far and hitting

the ends of travel and the tail servo is emitting

buzzing sounds, then decrease the LIMIT control.

It may be necessary to move the tail servo mount

on the tail boom or adjust a ball link or something

else to ensure that:

1) The tail servo can move the tail rotor pitch

from minimum to maximum without binding (e.g.

without the tail servo making a buzzing sound).

2) The tail servo should be centered when the

tail rotor pitch is at the middle of its range.

Be sure to reenable AVCS mode after setting the

LIMIT control.

Setting SENSITIVITY:

This is done at the transmitter on channel 5 for both

Futaba and JR radios. If you have a newer Futaba radio

(like a 9C) this is already handled in the GYRO SENS

menu. In this menu set the mode to AVC and the

sensitivity to about 50%.

If you have a Futaba/Hitec (negative shift) radio,

channel 5 settings below 50% are non-heading hold mode

sensitivity and settings above 50% are heading-hold

mode sensitivity. Initially, set your channel 5 to

about 88% travel.

If you have a JR (positive shift) radio, the settings

are swapped, e.g. below 50% is heading hold sensitivity

and above 50% is non-heading hold sensitivity.

Try setting your channel 50 to about 12% travel.

Yaw-Rate Gyro setup:

If using a separate yaw rate gyro (not Piccoboard):

You need need to enable the REVO MIXING feature

on the transmitter and adjust the REVO MIX curve

to effect revo mix changes.

If using any Piccoboard WITHOUT the heading hold module:

You will need to adjust the REVO MIX dial on the

Piccoboard to effect revo mix changes.

The revo mix controls the speed or pitch of the tail

rotor relative to the throttle position. This is

required to counteract the torque generated by the main

rotor blades so the heli does not yaw while in flight.

You will need to adjust the revo mix so the heli does

not yaw at all throttle positions.

The best way to do this is to buy a "lazy susan" type

turntable that will allow the helicopter to rotate

freely while the helicopter is weighed down so it won't

take off inadvertently. (Rubbermaid appears to make one

which is probably suitable)

Perform preflight checks, then slowly apply throttle.

The helicopter will start to yaw as you apply throttle.

You will need to adjust the revo mix so the heli has

no tendency to yaw as you slowly apply throttle.

It is normal for the tail to swing a little when

changing the throttle, as long as the heli does not

continuously rotate while the throttle is not changing.

If the helicopter is rotating and you need to increase

the thrust of the tail rotor to counteract the rotation,

then you should increase the revo mix at that throttle

position or turn right the revo mix dial on the

Piccoboard.

If the heli is rotating and you need to decrease the

push of the tail rotor to counteract the rotation,

then you should decrease the revo mix at that throttle

position or turn left the revo mix dial on the

Piccoboard.

m. Adjusting the blade grip bolts

1. Loosen the main blade grip bolts so the main blades

move freely.

2. Hold the helicopter so the right side or left side is

facing down.

3. Turn the main rotor hub so the blades are parallel to

the ground.

4. Tighten the blade grip bolts just enough so the blades

will stay parallel to the ground.

If you overtighten the main blade grip bolts, then the

main rotor blades will not straighten out at full headspeed

and this will cause vibration.

If you are having too many boom strikes later, you can tighten

the blade grip bolts after running up the heli to full

headspeed to ensure the blades have straightened out.

n. Adjusting main blade pitch

This step is only necessary for collective pitch helicopters

like the ECO 8/16 and Logo 10/16/20. This step is not necessary

for fixed pitch helicopters like the Piccolo FP and the Corona.

You should have a pitch gauge, either from the manufacturer of

your heli designed specifically for your heli or a

general-purpose helicopter pitch gauge.

1. Disconnect the heli motor from the ESC. Put some electrical

tape on the exposed connectors to insulate them so they will

not short out against each other or against other electrical

components.

NOTE: Do NOT use the throttle hold instead of disconnecting

the motor battery. Some transmitters (Futaba 9C) seem to

have a bug where if you adjust the pitch with the throttle

hold enabled, it does not save the settings correctly. So

don't use throttle hold and disconnect the motor wires

instead.

2. Put the pitch gauge on the helicopter following the

pitch gauge instructions.

3. Turn on the transmitter.

4. Connect the heli battery.

5. Adjust the blade pitch:

For hover practice, adjust the blade pitch so the pitch

range goes from 0 degrees at zero throttle to about 8 degrees

at full throttle.

For normal (non-inverted) flight, adjust the blade pitch so

the pitch range goes from -3 degrees at zero throttle to

10 degrees at full throttle.

6. Put the pitch gauge on the other blade and adjust

its blade pitch too.

o. Blade tracking - CP helicopters

If the pitch of the blades is not the same, then one blade

will generate more lift than the other when hovering.

This will cause vibration and steals power.

1. Temporarily put a piece of bright colored tape on one of

the rotor blades. This will cause the blades to be

unbalanced but don't worry about this for now. Just

remember to remove the tape after tracking the blades.

You need this tape to determine which blade is higher

or lower when checking the tracking.

1. Get a 6 foot length of 1" x 4" board.

2. Take the heli outside where the blades won't hit anything,

and slide the board through the landing gear on top of the

landing skids then either stake down the board or put

cinderblocks on it. The board will hold down the heli in

case Something Really Bad Happens.

3. Perform a preflight inspection and check everything.

4. Turn on the transmitter.

5. Connect the heli battery.

6. Arm the helicopter and slowly increase the throttle

to about 1/4.

7. Walk a safe distance away, then get on your stomach, and

apply throttle and look at the rotor blades from exactly the

side. If both rotor blades are spinning exactly in the same

plane and look like this: -- then no adjustments are needed.

If both rotor blades are not tracking in the same plane and

look like this: >< then the blades are not tracking properly

and require adjustment.

An alternative way to check the tracking is to place a

mirror on your feet, then tilt the mirror so you can see

the blades while standing up. This is considerably safer

since your face will not be hit if the heli decides

to throw a blade.

8. Shut off the throttle and wait for the rotor blades

to spin down.

9. Disconnect the heli battery.

10. If the blades did not track evenly, then increase the pitch

of the low blade and/or increase the pitch of the high

blade.

11. Go back to step 4 if necessary.

p. Blade tracking - FP helicopters

The Corona does not need blade tracking adjustments if you used

two 4 degree blade grips. The head mechanics are very stiff and

fairly precise which simplifies setup considerably. If you used

one 4 degree and one 6 degree blade grip, you should follow the

manual directions to set blade tracking.

The Piccolo FP has a soft rotor head and therefore the tracking

is frequently off. This is especially bad because bad tracking

steals a lot of power in micro helicopters.

To check the blade tracking on a Piccolo, temporarily put a

piece of bright colored tape on the leading edge of one of the

rotor blades. This will cause the blades to be unbalanced but

don't worry about this for now. Just remember to remove the

tape after tracking the blades. You need this tape to determine

which blade is higher or lower when checking the tracking.

Apply throttle and look at the rotor blades from exactly the

side. If both rotor blades are spinning exactly in the same

plane and look like this: -- then no adjustments are needed.

If both rotor blades are not tracking in the same plane and look

like this: >< then the blades are not tracking properly and

require adjustment.

The tracking of the stock Piccolo FP blades can be adjusted

by holding the blade firmly at the root and twisting the blade

at the widest point. Be sure not to twist the rotor head

(67370). You should increase the pitch on the low blade and

decrease the pitch on the high blade until the two blades

track evenly.

13. R/C heli rules/tips - read before hovering

a. Always turn on the transmitter and wait for it to transmit before

connecting the heli battery. If you connect the heli battery

without the transmitter on, it may go to full throttle which

may maim or kill you and/or nearby people.

b. Always turn off the heli before turning off the transmitter.

If you turn off the transmitter first, the heli may go to

full throttle which may maim or kill you and/or nearby people.

c. THE MAIN ROTOR BLADES ARE TRAVELING AT HIGH VELOCITY AND CAN

KILL OR MAIN YOU. BE VERY CAREFUL.

When I first stared flying helicopters, I read every single

web page I could find on the Internet regarding helicopters.

One web page mentioned a story where a guy was flying his

helicopter in a park, and a little dog started chasing his

helicopter around. The heli pilot asked the dog owner to retrieve

his dog, but the dog owner thought it was cute and wouldn't do it.

When the heli landed, the dog ran to the helicopter and lunged

at it. The main rotor blades were still spinning at full speed

and neatly chopped off the top of the dog's skull.

Also, there are stories about R/C helicopter rotor blades

chopping off people's fingers.

Don't believe it? Let's do the math.

An ECO 8 has a rotor diameter of 41.7 inches. This means the

rotor tips travel 41.7 * 3.14 or 130.9 inches in one revolution.

The rotor is spinning at about 1600 rpm. This means the rotor

tips travel 130.9 * 1600 or 209,440 inches in a minute.

In one hour the rotor tips will travel 60 * 209,440 or

12,566,400 inches.

12,566,400 inches/hr = 1,047,200 feet/hr = 198.3 mph!!!

So, when an ECO 8 rotor blade is spinning at 1600 rpm, the

blade tips are traveling at 198 mph. That's why helicopter

rotor blades can slice off fingers and the top of skulls.

RESPECT THE SPINNING ROTOR BLADES.

d. ALWAYS DISCONNECT THE BATTERY WHEN POSSIBLE IF WORKING ON

THE HELICOPTER. IF YOU MUST WORK ON A LIVE HELI, THEN

DISCONNECT AT LEAST ONE OF THE MOTOR LEADS SO THE MAIN

ROTOR/TAIL ROTOR WILL NOT SPIN UP AND MAIM YOU.

If the main rotor or tail rotor spins up and maims or kills

you, this will probably slow down your helicopter learning

process, so please try to avoid this.

e. A membership in your country's local R/C/ modeling club is

highly recommended because it provides insurance coverage

in case you damage something. This is very useful if your heli

damages somebody's car, or injures someone.

In the USA a membership in the Academy of Model Aeronautics

(AMA) provides insurance coverage.

In the UK the British Model Flying Association (BMFA)

provides this service.

14. Learning how to fly - the steps

The classical steps in learning to fly a heli are:

1. Tail-in hovering

2. Side-in hovering

3. Figure eights

These steps work well if you are already flying R/C planes.

15. Tail-in hovering

The first helicopter orientation to learn is "tail-in" hovering.

This is called tail-in because the tail of the helicopter will be

the closest to you.

a. Preparation

1. The most common helicopter "minor crash" is a boom strike.

This occurs the helicopter lands too hard and the main rotor

blade strikes the tail boom. It is advisable to have at

least one extra tail boom on hand to avoiding waiting

for parts.

2. You should have some practice time on a flight simulator.

This will really reduce the number of crashes and save you

A LOT of money.

3. You should have a training gear on your heli. The training

gear prevents the heli from tipping over and damaging

itself, and additionally makes the heli more stable by

slowing the cyclic response.

For a 1000-2000 gram heli, the best and cheapest training

gear can be made from a small hula-hoop and some 1/4 inch

dowels.  Do not use a dowel thicker than 1/4 inch, because

the 1/4 inch dowels will break in a hard landing and absorb

some of the impact.

a. Put the dowel across the diameter of the hula-hoop,

and cut the dowel so it's about 1 inch longer than

the diameter.

b. Cut another dowel the same length.

c. Use two tie-wraps to lash the two dowels together

in an X pattern.

d. Use tie wraps to attach the X to the hula-hoop.

e. Use tie-wraps or rubber bands to attach the X to the

landing gear of your helicopter.

f. Make sure the hula-hoop is on the bottom, so it will

slide along the floor on the hula-hoop.

4. The CG may shift when you attach the training gear, so be

sure to readjust the battery pack to move the forward/aft

CG back to the main rotor shaft.

b. Tail-in hovering - Phase 1

1. The objective for Phase 1 is to slide the helicopter around

on the ground to start building the hovering reflexes.

We do not want to lift off yet.

You will be learning the "tail-in" orientation, which is

the tail of the helicopter pointed towards you and the nose

away from you.

Be sure to focus on the nose of the helicopter, and not

the tail. If you focus on the tail, this is very bad.

You may want to stand slightly left or slightly right

of the helicopter so you can see the nose.

2. For a non-micro helicopter, find an empty flat space that

is fairly level and is fairly clean (no rocks or debris for

the training gear to hit).  You will need at least a 20 ft

by 20 ft area for this, although bigger is better.

An empty parking lot works well for this. Make sure there

are no cars nearby to ensure you won't hit them.

For a microheli, you probably want to find a hard level

indoor surface, possibly an empty garage or the kitchen.

A 10 ft by 10 ft surface is probably necessary.

3. Make sure wind conditions are ideal.

If you are using a heading hold gyro, then you want as

little wind as possible. The best times for this are

probably the first three hours of daylight or the last

hour of daylight before dusk.

If you are using a non-heading hold gyro, then you want

a little bit of steady breeze (not gusty) to help hold

the helicopter tail steady because the helicopter will

tend to turn when moving around. You will also want a

little bit of forward trim to compensate.

With either gyro type, make sure you point the heli nose

into the wind so the tail fin will help keep the heli

straight.

4. Place the helicopter and training gear on the ground, with

the nose of the helicopter pointed away from you.

5. Preflight check the helicopter. Make sure all ball links

are properly on the balls.

6. Turn on the radio. Make sure the transmitter is in

heading hold mode if using a gyro with remote mode

select, such as the GY401.

7. Make sure the throttle hold is enabled on the transmitter

and the throttle stick is fully down and the rudder is

centered. Connect the helicopter battery and wait for

the gyro to initialize.

The GY401 LED (light) should blink rapidly for about

two seconds, then switch to fully lit. If the LED

switches to a slow blink instead, then this is yaw

rate mode and your transmitter is not configured

correctly.

If the GY401 is powered-up in non-heading-hold mode, then

you will not be able to switch back and forth between

gyro modes. So, be very careful to power up the helicopter

while the transmitter is set to  heading hold mode.

8. Perform a radio range check and ensure all cyclic

servos move properly.

9. Make sure the throttle stick is completely down, then turn

off the throttle hold and arm the ESC (if necessary).

VERY, VERY SLOWLY apply enough power for the helicopter to

become light on the skids.  *** DO NOT LIFT OFF *** If you

accidentally lift off at this point, you will probably panic

and crash. So try not to lift off.

10. When you push the rudder stick left, the heli should rotate

counterclockwise. When you push the rudder stick right, it

should rotate clockwise. If these directions are reversed,

then you should fix the problem before continuing.

The rudder stick should control the NOSE of the helicopter

and not the tail.

11. The heli will start to wander around on its own. Use the

cyclic control to keep the helicopter within a 10 foot

circle.

12. The helicopter may have a constant tendency to move in

one direction, and you may need to apply some trim to

counteract this.

Note that it will be impossible to perfectly trim the

helicopter at this stage since you are hovering in ground

effect.

13. Always keep the tail of the helicopter pointed towards you.

If you are using a heading hold gyro, this should occur

automatically. If you are using a yaw rate gyro, you will

need to use the rudder to maintain the tail position

because the tail will tend to weathervane with the heli

movement.

14. Always fly the nose of the helicopter. This is very

important. Do not fly the tail. Always fly the nose

of the helicopter. When you give left rudder, the nose

should turn left, so always look at the nose.

15. For a non-Piccolo, use a very delicate touch on the

controls. The heli should be very responsive and respond

to very little pressure on the joystick. Use very light

stick pressure and avoid large stick movements.

The stock Piccolo requires a different technique. You will

need very quick half-stick movements with the joystick

to make corrections due to the slop in the swashplate.

16. If the helicopter starts to wander too far, reduce the

throttle to let the helicopter settle and stop moving.

Don't "chop" the throttle - reduce the throttle smoothly.

Later on when you are actually hovering, chopping the

throttle will cause the helicopter to crash. So, it's good

to not acquire this habit in the first place.

17. Focus your attention on the helicopter. Try to tune out

any distractions, and don't hold a conversation while

learning to hover. Think only of the helicopter and

its tilt and direction of movement.

18. It may help to watch the disk of the main rotor blades

because it will tell you if the helicopter is level.

19. When your nerves become frazzled, take a break.

Don't push yourself too hard, because you may lose

concentration and crash the helicopter.

20. When your batteries become weak, switch packs. Be sure

to wait a little while between flights to allow the

motor to cool down. For maximum battery life, let the

battery cool a little (about 5 mins) before recharging.

21. For a non-micro helicopter, when you can hold the heli

in a 10 foot circle, you are ready for the next phase.

For a microheli, you should be able to hold the heli in

a 3 foot circle.

c. Tail-in hovering - Phase 2

1. The objective for Phase 2 is to hover at 3-4 inches of

altitude (2-3 inches for a micro). Do not go any higher.

2. Go back to the hovering area, preflight the helicopter,

and perform range check/servo movement checks.

3. If you are using a heading hold gyro, then make sure there

is no wind or as little wind as possible.

If you have a non-heading hold gyro, you will need a slight

wind to help keep the tail steady. If you try to hover a

non-HH helicopter without wind, this will be very difficult

because the helicopter will "weathervane" into the direction

it's moving. This is very bad because you will need to

try to keep the tail steady while simultaneously hovering

the helicopter.

When hovering with wind, practice hovering with the

nose of the helicopter facing INTO the wind. When the

heli is facing into the wind, the vertical tail fin will

help keep the heli from turning (yawing).

3. Wait for the gyro to initialize, then arm the ESC.

4. SLOWLY apply enough throttle to lift the helicopter to the

desired altitude.

5. When the helicopter tilts, you will hear a scraping sound,

because the edge of the hula-hoop (or a ping-pong ball) will

drag along the asphalt (or carpet). Pay attention to this

sound, because it indicates your helicopter is tilted.

6. Watch the disk of the main rotor blades as they spin.

Try to keep the circle level, because when the circle is

level, your heli is level.

7. When the helicopter moves left, you should push the joystick

right to halt the movement, then when the helicopter has

stopped moving you need to nudge the joystick left to

level the helicopter. Same for the other three directions.

So, to stop a heli from moving in direction x requires two

small stick movements. This requires a while to learn

properly.

8. The helicopter may have a constant tendency to move in

one direction, and you may need to apply some trim to

counteract this.

Note that it will still be impossible to perfectly trim the

helicopter at this stage since you are hovering in ground

effect.

9. Try to avoid "overcontrolling" the helicopter. You want

to use small, delicate stick movements to gracefully

correct the movement. It takes a while to develop this

delicate, smooth touch. Be patient with yourself.

10. Try to keep the helicopter within a 10 foot circle, and try

to keep it level.

11. At some point, you will start to hover longer and longer

periods without an edge of the training gear touching the

pavement. This may require 5-10 battery charges or more.

12. Congrats. You're tail-in hovering. :)

13. When you can hold the heli within about a 5 ft circle,

you should practice hovering with the heli slightly to

the left of you or slightly to the right of you

(in about the 10 o'clock position and 2 o'clock position)

to prepare for the next section.

14. When you can hover an entire pack with tail-in hovering,

you should practice hovering at about 1 foot of altitude.

When you can hover at 1 foot very comfortably, you should

move to the next section.

16. Side-in and nose-in hovering orientations

The next step after tail-in hovering is side-in hovering. There are

two orientations for side-in hovering: left-in and right-in hovering

where the left side and the right side of the helicopter are facing

you, respectively.

You should make sure your tail-in hovering is fairly solid before

attempting side-in hovering. You will turn the heli back to the

tail-in orientation if you start to lose control, so make sure your

tail-in hovering is very solid before attempting this.

Follow the same steps as for tail-in hovering, except slowly turn

the heli to one side once you're hovering. You may want to start

with the heli only slightly turned, and slowly graduate to full

side-on orientation. If you "lose orientation" just use the tail

and turn the heli back to the tail-in position to avoid crashing.

Once you can hover both left-in and right-in hovering, you should

increase practice more on the weaker orientation to strengthen it.

This is very important to avoid developing "handedness" in orientation.

After left-in and right-in hovering, you might choose to learn nose-in

hovering. Some people say this is "very difficult" but really it's just

another orientation to learn. If you've learned three orientations,

you might as well learn the fourth before you go on to the next part.

It's probably okay to remove the training gear after you are fairly

comfortable with side-in hovering or nose-in hovering. The removal

of the training gear will change the flight characteristics of the

helicopter and make it more sensitive to stick input, so this will

require some mental adjustment. After you have removed the training

gear, you should hover at about 3ft to eye level.

I would recommend spending at least two months learning each hovering

orientation to ensure you are very comfortable with each orientation.

When you can hover entire packs with each orientation and feel

reasonably in control of the heli, you are probably ready to progress

to the next stage.

17. Additional orientation exercises

"...what flyers need most is solid fundamentals."

- Jason Krause interview, Model Helicopter Technique #36

The foundation of your helicopter flying skills is good orientation.

If you do not have good orientation skills, it will seriously hinder

your ability to learn forward flight and advanced skills.

Here are some exercises to practice which will help you close the

"orientation gaps" you may have. You may want to practice these in a

simulator first to become comfortable with them.

1. 90 degree yaw

While hovering, turn 90 degrees. Turn from either side-in to nose or

tail in, and back. Try to keep the helicopter stationary while

turning.

2. 180 degree yaw

While hovering, turn 180 degrees. Start with one side-in orientation

and switch to the other side-in orientation. Also, practice

switching from tail-in to nose-in and back, and tail-in to nose-in

and back. Try to keep the helicopter stationary while turning.

3. 45 degree nose-in orientations

The straight nose-in orientation easy, but the angled nose-in

orientations with the nose pointing 45 degrees left and right are

more difficult, so this is good to practice.

4. Single pirouette

While hovering tail-in/side-in/nose-in, execute a full 360 degree

yaw, and resume hovering. Be sure to practice both clockwise and

counterclockwise pirouettes to avoid developing "handedness".

5. Multiple slow pirouettes

These pirouettes should take about 16 seconds to complete a full

360 degree rotation. Try to keep the helicopter stationary while

performing the pirouettes. Be sure to practice both clockwise and

counterclockwise pirouettes to avoid developing "handedness".

18. Transmitter idle-up setup for fast forward flight

For a CP helicopter, you will want to program the idle-up mode on your

transmitter before attempting forward flight.

The idle-up mode allows you to keep a constant headspeed regardless

of the throttle position. This allows you to decrease and increase

the main rotor blade pitch without losing headspeed. This makes the

helicopter more responsive to altitude changes because the motor

will not change speed when the throttle stick is moved.

To set the idle-up, first look at your normal throttle curve, and note

the maximum throttle. For example, if your normal throttle curve is

0-50-85-85-85, then your max throttle is 85.

Next, switch to the throttle programming menu for the idle-up mode.

Set the throttle as a straight line across for the maximum value

in your normal throttle curve; in this case it would be 85-85-85-85-85.

Now, when you spool up your helicopter, you will do it in the normal

throttle position until you reach full speed. When the full speed

is reached, you will flip over to the idle-up mode to start flying.

When you land (or crash) and need to turn off the motor, use the

throttle hold switch. This will take a little bit of practice.

19. Entering/exiting fast forward flight

Forward flight is a little tricky on helicopters. It requires

simultaneous coordination of both the throttle and cyclic to enter

and exit forward flight smoothly.

To enter forward flight, it is necessary to tilt the heli forward

(use forward cyclic) and simultaneously apply a little throttle.

If you tilt the heli forward without applying throttle, the helicopter

will slide nose-first into the ground. This is because the thrust from

the heli is being vectored at an angle relative to the ground, and you

lose some vertical lift because it's being converted to horizontal

thrust.

Once the helicopter starts moving, you will need to tilt the heli

back a little and simultaneously reduce throttle below hover.

You will need to reduce the throttle because translational lift will

occur and you will now get extra lift.

Exiting forward flight into a hover is the reverse process. You will

need to tilt the heli back (use back cyclic) to reduce forward motion,

and simultaneously reduce throttle to prevent the heli from climbing up.

After the forward motion has been reduced, you will need to level the

helicopter (use forward cyclic) and add throttle to transition to

a stable hover.

One way to practice forward flight is to pick two points a comfortable

distance apart (maybe five feet for a micro, ten or fifteen feet for

a nonmicro) then practice flying back and forth between those two

points (stop into a hover at each point and turn 180 degrees).

20. Banked forward turns

Banked turns are also a little tricky, and requires simultaneous

coordination of the throttle and cyclic as well.

The first phase of a banked turn is to apply left or right

cyclic in the direction of the turn until the desired bank angle

is reached.

The second phase of a banked turn is to simultaneously apply

back cyclic and rudder in the direction of the turn.

The third phase is to straighten out after the turn. This requires

using forward cyclic to maintain forward motion and centering the

rudder stick.

21. Figure eights

This is a combination of the forward flight and banked turn skills.

This is a bit tricky on the Corona because it does not turn well when

the main rotor is throttled down, because the tail rotor is also

throttled down. If you try to do turns when the tail is throttled down,

it will turn very slowly then snap into position when the helicopter

enters forward flight.

To do proper figure eights on the Corona, you will need to throttle up

slightly when entering turns to ensure the tail has enough authority

to turn the Corona, and throttle down slightly when exiting the turn

and entering the forward flight section.

Practice easy figure eights first where the heli turns tail-in at

both ends of the figure eight. Once you are comfortable with these,

try the hard figure eights where the heli turns nose-in towards you.

BE SURE to attempt the nose-in turns at a reasonable distance from

yourself to avoid hitting yourself with the helicopter!

For added complexity, try doing a pirouette or two in the middle of

the forward flight section of the figure-eight.

22. Backwards flight

"I always lead with the tail. As I watch the heli I'm keying off the

tail, as far as I know, and I steer along with the tail."

- Todd Bennett, Model Helicopter Technique #35

Backwards flight is tricky because it requires unlearning some of

the reflexes learned for forward flight. You will need to fly backwards

by concentrating on the tail of the helicopter (not the nose!), and

the controls to slow down and speed up are reversed.

You will need to be very careful about letting the tail tilt too

low, because it will hit the ground and flip the helicopter over.

If you don't have a good heading hold gyro by this point, I highly

recommend you buy one now. Backwards flight is much more difficult

without heading hold because the tail will have a strong tendency

to weathervane suddenly and flip around, which can cause you to

lose orientation and crash.

You may want to perform the "fly between two points" exercise

mentioned in the forward flight section in a backwards orientation

to become comfortable with backwards flight.

23. Banked backwards turns

Banked backwards turns are tricky because the cyclic does not follow

the rudder...it is the opposite of the rudder. This requires a bit

of explanation.

For forwards flight, a left turn consists of left rudder with LEFT

cyclic, because the left side of the helicopter faces the inside

of the loop.

For backwards flight, a left turn consists of left rudder with

RIGHT cyclic, because the right side of the helicopter faces the

inside of the loop.

There are two turns in two orientations, which results in

four backward turns:

1. Right turn where heli is tail-in relative to you

(e.g. heli is traveling from your left to your right,

then makes a right turn towards you)

2. Left turn where heli is tail-in relative to you

(e.g. heli is traveling from your right to your left,

then makes a left turn towards you)

3. Right turn where heli is nose-in relative to you

(e.g. heli is traveling from your right to your left,

then makes a right turn away from you)

4. Left turn where heli is nose-in relative to you

(e.g. heli is traveling from your left to your right,

then makes a left turn away from you)

The potential for crashing is pretty high, so I highly recommend

practicing these in a simulator before trying them on your heli.

I recommend learning the tail-in turns before the nose-in turns

because the tail-in turns are easier.

When performing backwards turns, there are three things you

need to watch simultaneously:

1. The bank of the helicopter. If the helicopter banks too much

then it will lose lift and slide into the ground.

2. The angle of the tail. If the tail sinks too low then your

heli will dive into the ground.

3. The yaw rate. If you yaw too much, you will wind up merely

performing pirouettes, and if you yaw too little the turn

will look sloppy.

24. Backwards exercises

A "remote circle" in this section means flying in a circle

not around yourself, but at some distance away.

1. Backwards remote half circles

Fly in a circle, but fly only half of it backwards.

So, you will need to perform two 180 degree pirouettes during

the circle to change orientation.

This is easier than a backwards full circle because you can

learn the tail-in backwards turn first, which is easier.

For a clockwise circle, do the right half of it with a backwards

orientation. For a counterclockwise circle, do the left half

with a backwards orientation.

2. Backwards remote full circles

Fly in a full circle backwards. Try to keep the helicopter moving

smoothly at a constant speed. Be sure to practice both clockwise and

counterclockwise circles.

3. Backwards tail-in figure-eight

Fly in a figure-eight backwards where the heli turns nose-in

to you during the turn.

4. Backwards nose-in figure-eight

Fly in a figure-eight backwards where the heli turns nose-in

to you during the turn.

25. Maintenance and Crash Repair

1. Brushed motors w/carbon brushes

After every ten flights or so, the carbon dust should be blown

out of the motor with compressed air and the commutator checked

to see if it is clean. If the motor is assembled with screws

and the commutator is dirty, disassemble the motor and burnish

the commutator with some extra fine steel wool or 1000-1200 grit

sandpaper.

2. Main rotor shaft bearings

Some helicopters (ECO, etc) have open-faced bearings. These

bearings are not sealed, and because the ball-bearings are

exposed, they can become contaminated with dirt and grit.

If you notice the main rotor shaft bearings grinding or not

rotating smoothly, then they should be removed and cleaned in

some good solvent or cleaned with compressed air. If they still

sound or feel funny, they should be replaced.

3. Tail rotor shaft bearings

The tail rotor shaft bearings may incur damage if the tail

blades touch the ground, especially on the ECO 8/16. They should

also be checked periodically and cleaned or replaced if

necessary.

4. Tail belt tension

Tail belts tend to loosen over time especially if the tail boom

mount is loose. They should be checked and retensioned

periodically.

5. O-rings

O-rings will last longer if they are unhooked from the battery

mounts when not in use. If they are left under tension continously,

they will develop cracks over time. The O-rings should be checked

periodically and replaced if necessary.

6. Main rotor blades

If the main rotor blades appear damaged do NOT fly with them.

They can explode in flight which is very dangerous.

You should replace any blades which appear damaged.

Corona specific maintenance:

a. If you have a boom strike, the tail boom can be straightened by

pushing a 3/8" dowel inside the tail boom.

b. If you let the Corona come down too fast it may "bounce" off the

ground and break a main gear tooth and/or trash a bearing. So,

the main gear should be checked periodically for missing teeth

and the main rotor shaft bearings should be checked for smoothness.

c. Be sure to check HS-81s for broken gear teeth after each hard crash.

They may rotate properly through the whole rotation, but they may

have a broken tooth somewhere.

I consider the HS-81 gears a "sacrificial" part...they break to

prevent other things from being broken, and at $3-$5 a set they are

fairly cheap.

Piccolo specific maintenance:

a. There isn't much maintenance required on a Piccolo. The stock brushed

motor (the 280 or 310) should last 300 flights or more without

maintenance if properly broken-in.

b. If the antirotation pin breaks off the swashplate but the stub

is left, then it can be fixed with a small nylon tiewrap. Cut the

tip from the tie-wrap and lash it the remnants of the antirotation

pin by using several loops of cotton thread. After tying, put a

drop of thin CA on the thread to harden it.

ECO 8/16 specific maintenance:

a. The one-way bearing in both plastic and aluminum autorotation hubs

has been known to become loose. Usually when this happens, the

one-way bearing can be pushed out of the hub with firm finger

pressure.

This can be easily fixed by roughing up the bearing and autorotation

hub mating surfaces with 200 grit sandpaper and using thick CA to

reassemble the unit.

b. The tail blade grips (67542) should be checked periodically to make

sure they are not too loose. If they are, be sure to unscrew them

from the tail rotor hub and apply fresh loctite to the screw before

reassembling.

c. The main rotor shaft bolt (67599) is rather soft and can become bent

in a hard crash. Be sure to check this bolt if the main rotor

blades have hit anything. If the bolt is bent, be sure to replace it

and do not fly with it.

d. The battery holder O-rings (67587) will need to be replaced about

once a year because they will start to crack. These can be replaced

with the stock Ikarus parts or you may be able to find the O-rings

(30mm ID x 3mm thick) cheaper elsewhere.

26. Troubleshooting common problems

1. Motor ESC will not arm, or motor continues to run at zero throttle

a. If you are using a Futaba transmitter, you will need to

reverse the throttle channel on the transmitter.

b. You may need to decrease the "zero throttle" endpoint

to arm the ESC properly. This is a common problem with the

Castle Creations ESCs, but also happens occasionally with

the Schulze ESCs as well.

2. Short flight times and/or not enough power

a. For brushed motors: the commmutator may be dirty.

See section on maintenance.

b. Pinion meshing may be too tight. The pinion should not be

firmly fitted against the main gear. The motor pinion should

be able to wiggle just a tiny bit without turning the main

gear.

c. Motor pinion may be slipping on motor shaft.

If your motor pinion uses a setscrew, then your motor should

have a flat spot on the motor shaft so the setscrew will

not slip on the motor shaft.

If the motor shaft has no flat spot for the setscrew

to bite, then you should make one with a Dremel and a

diamond cylinder point bit (#7123).

For the Piccolo using the stock motor (G280 or G310)

and the plastic motor pinions, it may be necessary to glue

the plastic pinion onto the motor shaft to prevent it

from slipping.

d. Woodies may be trashed

Most larger wooden blades are made of a hardwood leading

edge and a balsa trailing edge all shrinkwrapped together.

On hard crashes, the balsa part can be severely damaged

but the blade looks fine due to the shrinkwrap holding

the blade together.

If you look closely you may be able to see the breaks

in the balsa. If you can see this, then the blade should

be replaced.

3. Heli has excessive vibrations

If you follow these directions step-by-step, you should

be able to solve most vibration problems.

The basic methodology is to keep removing parts off the

helicopter until the vibration stops, and when the

vibration stops the last piece you removed was causing

the vibration problem.

a. Check the obvious

Check if main gear mesh is too tight.

Check if the main gear is missing teeth.

Check if the tail belt is too loose or too tight.

b. Check main blade tracking.

Put a piece of marking tape on one blade and run up the

motor. Check if the blades are tracking properly. If the

blades do not track properly, then see the section on

blade tracking.

c. Check if the blade grip bolts are too tight

Hold the helicopter so the right side or left side is

facing down, and see if the main rotor blades will

stay horizontal to the ground. If they just barely stay

horizontal then this is just right.

d. Check main rotor blade CG and balance

Balance the main blades on a blade balancer and ensure

the CGs match and the blades balance. If the CG does not

match or the blades do not balance, then see the section

on blade balancing.

e. Check if the feathering shaft is bent

Disasemble the main rotor hub and remove the feathering

shaft. Roll the feathering shaft on a sheet of glass to

check if the shaft is bent.

The Corona doesn't have a feathering shaft, and instead

has an aluminum rod which holds the subrotor on the rotor

hub. This rod is very thin and has a tendency to bend

after a few crashes. You will notice this because the

subrotor paddles will "droop down" and will not be

parallel to each other.

This problem can be easily fixed by carefully bending

the subrotor paddles up to straighten the aluminum rod or

bye replacing the aluminum rod.

f. Check if the rotor head is balanced

Reinstall the head and swashplate assembly but remove

the main rotor blades. Connect the battery and slowly apply

throttle. If the heli is vibrating then you should check if

the flybar is straight and centered and balance the main

rotor head using a Tru-spin prop balancer or equivalent.

g. Check if the main shaft is bent

Remove the main rotor head, swashplate and all the related

linkages. Run up the motor without the head and hold

a screwdriver against the top of the shaft as the shaft

turns. If you feel vibration while holding the screwdriver

against the turning shaft, then the shaft is bent.

Alternatively remove the head and swashplate assembly and

remove the main shaft. Roll the main shaft on a sheet of

glass and check if the main rotor shaft is bent.

h. Check the main rotor bearings

Remove the main shaft bearings from the helicopter.

Put the main shaft through each bearing and spin it by hand.

If the bearing does not rotate smoothly or feels gritty,

then replace it.

i. Check tail rotor blade balance

Reinstall the main rotor shaft and main gear, but do

not reinstall the head and swashplate assembly.

Remove the tail rotor blades and run up the helicopter.

If the vibrations are gone, then the tail blades need to

be balanced  or replaced.

j. Check the tail rotor bearings

Remove the tail shaft bearings from the helicopter.

Put the tail shaft through each bearing and spin it by hand.

If the bearing does not rotate smoothly or feels gritty,

then replace it.

k. Tail rotor hub balancing

If the vibrations remain, then the tail rotor shaft and

hub need to be balanced. Put the entire assembly on a

Tru-spin prop balancer or equivalent for balancing.

4. Heli hovers slightly tilted to the right (or left)

a. This is normal. The helicopter will tilt slightly due to the

thrust of the tail rotor.

5. Heli wobbles and is very unstable

a. Your headspeed may be too low and you may be compensating

for this by using more main motor pitch which makes the

heli motor bog down and the heli unstable.

b. Your rotor head may not be firmly attached to the main rotor

shaft. This usually occurs when the hole in the rotor head

is reamed out after multiple hard crashes. If the rotor head

is not fitting snugly on the main rotor shaft, it should be

replaced. This problem is seen on MS Hornets. because the

E044 pivot support is fragile.

6. The blade tracking is fine at low speeds, but the blade tracking

becomes worse at high head speeds.

a. On a CP Piccolo, this is usually caused by a broken pitch

arm base (68211). Visually inspect the two thin "legs" which

are between the arms and the tube. One of the legs may have

broken.

b. The feathering shaft may be bent. Disassemble the head

and put the feathering shaft in a drill and spin it

to check if the shaft is bent.

7. Tail jerks around when spooling up with HH gyro

a. The gyro may be too close to the ESC.  On a non-micro heli,

the gyro should be at least four inches away from the ESC.

b. Tail belt may be twisted around. Removing the tail rotor

assembly from the tail boom and make sure the tail drive

belt isn't twisted.

8. Cyclic servos wiggle around without joystick input when motor

is running at or near hovering throttle.

a. This could be radio interference. Make sure your motor

leads are short and routed away from the receiver.

b. With a brushed motor, the motor brushes may be worn or

the commutator may be dirty which causes radio interference.

Check your brushes and make sure they are in good condition

and check the condition of the commutator.

9. Tail wags constantly with HH gyro

a. The gyro gain may be set too high. Try lowering the gyro

gain until the wagging stops.

b. The main gear or other gear may be missing a tooth.

Visually inspect the teeth of all gears and verify they

are all intact.

c. Tail belt may be loose. The belt should be firm but not too

tight.

d. Excessive play in the tail pitch control system can cause

tail wag. Make sure there are no loose screws/ball links/

clevises in the tail pitch control system.

(A little play is normal, but not too much)

e. The tail rotor shaft may be dirty and the pitch slider may

not be sliding smoothly on the shaft.

This is fairly easy to fix. Remove the tail rotor shaft

and throughly remove all gunk using some tissue paper.

A cotton swab stick is just under 2mm in diameter, so cut

a cotton swab in half and use the two stick sides to clean

the inside of the tail pitch slider.

Do NOT apply any oil to the tail pitch slider because it

will become dirty extremely quickly. If lubrication is

needed then use powdered graphite instead.

e. The tail blade grip bearings may be dirty and/or damaged,

or loctited to screw.

f. The tail blade grip screw may be bent.

g. Make sure the servo is mounted securely to the frame

or tail boom mount. Check for loose or stripped screws.

h. Make sure there are not rubber servo grommets used for

the tail servo mounting. This can cause wag.

i. Try replacing the tail servo. The potentiometer on some

servos will wear quickly with constant movement, and this

can cause wag.

j. Check if the gyro is mounted securely to the frame. If the

gyro is not mounted firmly with servo tape, then it can

wobble back and forth which can cause wag.

10. Tail swings 30-90 degrees abruptly then rights itself with HH gyro

while hovering.

a. This could be caused by radio glitches. Make sure your

motor leads are short and routed away from the receiver.

b. The radio receiver crystal may have been damaged in

a previous crash. Try replacing the crystal or entire

receiver.

c. The one-way bearing in the autorotation hub may be loose.

11. Tail servo responds properly when tail swings one direction but

tail servo fails to respond in other direction.

a. The gyro may be damaged.

12. Heli twitches randomly in roll/pitch/yaw

a. This can be caused by radio interference.

This can be diagnosed by temporarily wrapping the radio

or gyro in aluminum foil to see if the glitching stops.

if the glitching stops, then this component is probably

too close to the motor and/or ESC and should be moved

to a different location.

27. Useful equations

This is a section with various bits of math which are useful for

calculating various parameters of helicopters.

a. Calculating headspeed

This is fairly easy to do. It's basically the motor speed multiplied

by the gear ratio, or stated as an equation:

headspeed = (motor Kv) * (battery voltage) * (percent throttle / 100)

* (motor pinion teeth) / (main gear teeth)

For example, consider a Hacker B50-18S in an ECO using 8 cells with

a 18 tooth pinion, at 85% throttle.

headspeed = 2006 * 9.6 * .85 * 18 / 180 = 1636 rpm

Given two otherwise identical motors with different Kv, the one with

the higher Kv will usually be more powerful because the resistance of

the windings is lower and therefore it can draw more current.

Therefore, a motor with a higher Kv using a lower tooth pinion is

better for power and sport flying whereas a motor with a lower Kv

using a higher tooth pinion is better for duration flying.

b. Estimating amperage draw

Helicopters generally need about 100 watts per kg to hover.

This can vary by about 20-30% depending on the drivetrain,

blade airfoil, motor efficiency, etc.

So, given the helicopter's weight and cells:

estimated amp draw = (helicopter AUW in grams) / voltage

An ECO 8 AUW is around 1500 grams, and uses 8 cells, so:

estimated amp draw = 1500 / (9.6 * 10) = 15.6 amps

The more efficient electrics (ECO 8/16) will use a little less, or

about 80-90 watts/kg. The gas-to-electric converesions will be at

the high-end of the scale, or about 120 watts/kg.

Note: This amperage figure is NOT the maximum required during

hovering, only the average figure. For example, if you reduce power

while hovering and the helicopter starts descending in its own

downwash, then you will need substantially more current to halt

the descent because the blades are less efficient in turbulent air.

Therefore, you need a battery/ESC combo that can handle about twice

the hovering current in order to have a reasonably safety margin for

recovering from bad situations.

28. Electric Helicopter & parts vendors

These are vendors which are mentioned frequently on various popular

Internet discussion forums.

I do not necessarily endorse any vendors on this list.

For brevity, any e-heli vendors who also stock servos/motors/etc.

will not be listed again in the servos/motors/etc section.

a. Lite Machines Corona and replacement parts

http://www.litemachines.com

http://www.roffeetvhobby.com

http://www.rc-city.de

b. Mikado Logo 10

http://www.fxaeromodels.com

http://www.cyberheli.com

http://www.heliguys.com

http://www.aero-model.com

http://www.rc-city.de

http://www.cyberheli.com

c. Ikarus ECO Piccolo and Piccolo Fun

http://www.dreamhobbies.com

http://www.precisionmodelproducts.com

http://www.fxaeromodels.com

http://www.helihobby.com

http://www.hobby-lobby.com

http://www.rc-city.de

d. Ikarus ECO 8/16

http://www.fxaeromodels.com

http://www.precisionmodelproducts.com

http://www.hobby-lobby.com

http://www.helihobby.com

http://www.rc-city.de

e. MS Composit Hornet

http://www.fxaeromodels.com

http://www.precisionmodelproducts.com

http://www.edogfight.com

http://www.aeromicro.com

http://www.helihobby.com

http://www.hobby-lobby.com

http://www.rc-city.de

f. Motor vendors

http://www.towerhobbies.com

http://www.icare-rc.com

http://www.megamotorusa.com

http://www.aveox.com

http://www.overlander.co.uk

http://www.hackerbrushless.com

http://www.rumrunnerhobbies.com

(Also check the rcgroups sponsor links)

g. Servo vendors

http://www.servo-city.com

http://www.balsaproducts.com

http://www.nesail.com

http://www.towerhobbies.com

http://www.horizonhobby.com

http://www.shredair.com

http://www.hobbyclub.com

h. Batteries and related supplies

http://www.dynamoelectrics.com

http://www.batterystation.com

http://www.eflightpacks.com

http://www.nicdlady.com

http://www.modelelectronicscorp.com

i. Carbon Fiber tubes and rods

http://www.cstsales.com

http://www.acp-composites.com

j. Other

http://www.microheli.com

http://www.modelaircraft.org (AMA)

http://ks.jp.org	(K&S aftermarket parts)

http://www.ircha.org	(Int'l Radio Controlled Helicopter Assoc)

k. Useful webpages & Forums

RCgroups  discussion forums	http://www.rcgroups.com

Paul Goelz's Piccolo site	http://www.pgoelz.com

Glen Peden's Logo site		http://www.logoheli.com

Piccolo and ECO 8/16 forums	http://www.ikarus-germany.com

ECO 8/16 information		http://www.dream-models.com

MS Composit Hornet Forums	http://www.hornet-heli.com

brushless motor info:

http://www.dokidoki.ne.jp/home2/tohrus/motorindexE.html

Helicopter rotor head dynamics:

http://www.dokidoki.ne.jp/home2/tohrus/heli-00/rotorhd-study.html

Aerobatics:

http://www.dokidoki.ne.jp/home2/tohrus/heli-00/acro-tech-e.html

http://www.dokidoki.ne.jp/home2/tohrus/heli-00/invertedE.html

l. Magazines

Rotory				http://www.rotory.com

Model Helicopter World		http://www.modelheliworld.com

Model Helicopter Technique	http://www.mht.net

29. Terminology

120 CCPM

A type of CCPM using three servos arranged at equal 120 degrees

from each other. The advantage of 120 CCPM is the load of the

swashplate is evenly distributed across all three servos

resulting in more precise control. 120 CCPM requires a

special transmitter ("computer radio") which supports this mode.

90 CCPM

A type of CCPM using three servos arranged at 90 degrees to

each other (and one spot empty). On an ECO 8/16 using 90 CCPM

there is a servo at the left, right, and front positions

of the swashplate.

AR pin	Antirotation pin.

AR arm	Antirotation arm.

Autorotation

A controlled, unpowered helicopter descent (and landing).

A helicopter is a brick with a rotor, so it doesn't glide

well when unpowered. The autorotation is the closest to

gliding possible. The autorotation consists of a steep descent

using negative pitch to keep the rotor blades spinning

followed by a slight flaring performed with positive pitch

to convert the momentum of the blades into lift to soften

the landing.

Autorotation gear

Autorotation gear. A gear with a one-way bearing so the motor

can only drive the main shaft in one rotational direction.

Required for performing autorotations.

AR gear

See autorotation gear.

AUW 	All-Up Weight. The weight of the heli when ready to fly,

including batteries.

ball-link pliers

A special plier made especially for handling ball links.

It can quickly remove the ball joint from a ball link without

damaging either part. One jaw has a U-shaped cut in it and

the other jaw has a small cup on it to hold the ball joint.

BEC	Battery Eliminator Circuit. This circuitry takes the voltage

from the battery pack (which is higher than 4.8 volts)

and reduces it down to the 4.8 volts required by the

gyro, the receiver, and the servos.

Bell-Hiller mixer

The seesaw arm on the head of a CCPM helicopter which isolates

the height component of the swashplate position and controls

the main blade pitch.

BL	Brushless, usually in the context of brushless motors.

Boom strike

A type of helicopter crash where the main rotor blade hits

the tailboom. This may dent/bend the tail boom and damage

the main rotor blades.

Collective Pitch Compensator

The assembly with two seesaw arms directly above the swashplate.

CCPM	Cyclic/Collective Pitch Mixing. A type of control system where

the swashplate controls both main blade pitch and flybar

pitch. The swashplate relative tilt controls the pitch of the

flybar as the main rotor rotates, and the absolute height

of the swashplate controls the pitch of the main rotor blades.

CF	Carbon fiber, usually in the context of rotor blades, frames,

tubes, rods, or sheets.

CG	Center of Gravity. The point at which an object's center of

mass appears to be; its balance point.

Coning Angle

Some helicopters like the FP Piccolo are designed so the

rotor blades are flexible and will bend upwards in flight.

The amount which the blade bends upwards is called the

"coning angle". The coning effect is good for beginner

helicopters because it makes hovering more stable, but

is bad for forward flight because it makes the helicopter

pitch up which makes forward flight difficult.

CP	Collective Pitch. A helicopter that adjust vertical lift by

changing the pitch of the main rotor blades.

Disc loading

The weight of the helicopter divided by the rotor disc size.

Similar to the "wing loading" figure for airplanes.

"High disc loading" means the helicopter is heavy for its

rotor size, or conversely, the main rotor blades are short

for its weight.

eheli	Electric Helicopter - hard to figure out, isn't it?

Electronic Mixing

A control system where the radio transmitter controls the

mixing between the roll/pitch servos and the main rotor pitch

servo. Also called colloquially eCCPM. See also CCPM.

ESC	Electronic Speed Control. Basically, the motor controller

for brushed and brushless motors.

ESD	Electrostatic Discharge. This usually refers to the static

electricity which builds up on the tail belt, most often on

Logo 10s. Some people have reported "ball lighting" shooting

away from Logo 10s on humid days.

Flybar	The metal or CF rod which holds the smaller paddles to the

main rotor head

Flybar paddles

The smaller blades (not the main rotor blades) on the main

rotor of a helicopter.

FF	Forward Flight.

FP	Fixed Pitch. A helicopter that adjusts altitude by changing

the speed of the motor driving the main rotor.

GE	Ground Effect. When a helicopter is hovering at approximately

less than one rotor length above the ground, the heli will

become a little more skittish, as though it is trying to

balance on a ball. This is the ground effect.

GF	Glass fiber (fiberglass) usually in the context of rotor blades.

Governor

A feature of an ESC which will try to keep the motor speed

constant despite variable load placed on the motor.

This is like the cruise control on a car as it's going up

and down hills. Even though the load on the motor is variable

as the car goes up and down hills, the cruise control will

try to maintain the same speed.

The governor mode on an ESC will try to do something similar.

Even if the heli is doing wild maneuvers and the load on

the main rotor blade is highly variable, it will try to

maintain a constant head speed.

If using a governor mode, the throttle curve should not

be set to 100%. This is because the governor mode needs

a little bit of extra power so it can maintain headspeed.

Using the cruise control analogy, if you set the cruise control

of a car to its maximum speed the cruise control cannot maintain

the maximum speed going up hills. Similarly, if you set

the throttle to 100% RPM then the governor mode will not

be able to maintain it when the rotor is heavily loaded.

This is why the motor pinion should be selected so the desired

headspeed can be achieved at 90 to 95% of the throttle - so

the governor mode can work properly.

Heading Hold Gyro

A gyro which attempts to "lock" the heading of the gyro

and keep the helicopter pointed in the same direction

until you choose to turn it via the rudder. See yaw-rate gyro

also.

HH	Heading Hold (gyro)

HS	Head Speed. The RPM of the main rotor. Most helicopters need

between 1200-2000 RPM of headspeed to fly. If the headspeed is

too low, then the heli will not lift off or will require extra

pitch to fly, which will make the heli very unstable. For aerobatics,

most people raise their headspeed to about 1800-20000 RPM. Most

helicopter rotor hubs are only rated for a maximum of 2000 RPM.

If you exceed 2000 RPM, this places excessive stress on the main

rotor hub and the heli is likely to throw a blade.

Hunting	See Wag.

idle-up mode

A transmitter mode which has a different throttle and pitch

curve than the regular mode. For electric helicopters, we

normally use the "normal" mode to arm the ESC and spool up

the helicopter, and use an idle-up mode with a flat throttle

setting for regular flying.

Some transmitters have multiple idle-up modes. For example,

the Futaba 9C has idle-up1, idle-up2, and idle-up3 modes.

The additional idle-up modes can be programmed for a low

headspeed for duration flight, high headspeed with full

negative pitch range for aerobatics, etc.

Kv	The RPM per volt of the motor. This is very important because

a helicopter typically requires a headspeed of about 1400-1800

RPM to hover/fly properly.

Lead/Lag bolt

The bolt which allows the main rotor blades to swing

horizontally so it can either lead (swing ahead) or lag

(swing behind) the main rotor head.

LHS	Local Hobby Shop

LVC	The low-voltage cutoff point of the ESC, if it has one.

For a heli, you want an ESC with no or very low LVC.

Mechanical mixing

A type of control system where the roll/pitch and main blade

pitch are not mixed at the transmitter but are instead mixed

mechanically at the helicopter. See also CCPM.

Micro helicopter

This is a rather subjective term, but in this guide it refers

to any helicopter under 400 grams AUW. This includes the

Ikarus Piccolos, MS Hornets, Century Hummingbird, Feda,

GWS Dragonfly, MIA Housefly, Wes-Technik Helistar LH35, etc.

Revo mix/Revo mixing

A mixer which adds a percentage of the main rotor throttle

to the tail rotor throttle to prevent the heli from spinning.

This is only used with yaw rate (non-heading hold) gyros

because the yaw rate gyro only dampens tail movement and cannot

maintain the direction of the tail. If using a heading hold

gyro, this option should be DISABLED on the transmitter.

RFI 	Radio Frequency Interference. RFI causes little "glitches"

in your control and the heli will twitch abruptly in one

direction or another and/or the tail may suddenly jerk around.

Swashplate

The control mechanism component which mechanically joins the

non-rotating control portions to the rotating control portions

of the main rotor.

Throttle hold (switch)

For electric helicopters, this switch is usually set to force

a zero throttle setting regardless of the throttle stick

position. This is useful as a safety switch to prevent the

motor from spooling up while connecting the battery, and also

to quickly kill the motor when the helicopter is crashing

when using an idle-up mode.

Throw a blade

Refers to a main rotor blade being flung off the rotor head

(usually with the blade grip) at very high speed while the

head is spinning. This is very, very dangerous.

TL	Translational Lift. The extra lift produced by the main rotor

when a helicopter is moving horizontally or when hovering

in windy conditions. When a helicopter stops moving horizontally

it tends to drop, because it loses the extra lift.

TR	Tail rotor.

Wag	A rhythmic back-and-forth tail movement that will not stop.

This may occur with heading hold gyros when the setup is

not correct. In this case, the gyro overshoots the correct tail

position, so it constantly keeps omving the tail.

Woodies	Wooden main rotor blades.

Yaw-rate gyro

A type of gyro which dampens but not eliminates unwanted

yaw rotation. If a gust of wind blows the tail of a helicopter

with a yaw-rate gyro, the gyro will make the tail rotor

"push back" against the wind to reduce the amount of unwanted

tail movement, but since it does not keep track of total

tail movement, it cannot return the tail back to its original

position.