Click an Image to Enlarge

This auction is for a 1/10 RC car / truck / buggy brushless motor combo

Proudly presented by SKYRC, Leopard Series

Fit on most 1/10 RC car, steady and reliable!

Specification
MOTOR

| Item Name | Leopard 3300KV/12T/2P BL Motor for 1/10 Car |
| --- | --- |
| Sensored /Sensorless | sensorless | No loading @7.2V Current | 1.2A |
| Turns | 12T | Max current | 51A |
| KV value | 3300KV | Resistance (O) | 0.0246O |
| Poles | 2P | Battery range | 1-3S |
| Diameter | 36mm | Operation Temperature | / |
| Motor length | 50mm | Max Temperature | 150° |
| Extend shaft diameter | 3.165mm | Suitable car scale | 1/10 |
| Length of extend shaft | 15mm | Suitable ESC | 35A or higher |
| Weight | 176g | Connector Type | 3.5mm |

Leopard 60A v2.0 ESC

| Controls, Leopard 60A ESC V2 | Fwd/Brk or Fwd/Bra/Rev |
| --- | --- |
| Input Power (Cells) | 2-3S LiPo,4-8S NiCd/NiMh |
| On Resistance, Brushless | 0.001 Ohms per phase |
| Continuous/Burst Current | 60Amp/90Amp |
| Linear BEC | 5V 2Amp |
| Input Power (Cells) 2S LiPo 3S LiPo | Motor Limits On Road:=9.0T Off Road:=10.0T On Road:=10.0T Off Road:=13.0T |
| Thermal Overload Protection | Yes |
| Dimensions(L*W*H) | 51.6*30*27.4mm(2.03*1.18*1.08in) |
| Weight(With wires) | 78g(2.75oz) |

TORO Program Card

Specifications: